## STATus
### STATus:OPERation[:EVENt]?
Syntax	STATus:OPERation[:EVENt]?
Description	This query returns the value of the read-only Operation Status Event register The bits are latched and reading the register will clear it. The *CLS command can be also used to clear the register.
Return	The value returned is the binary-weighted sum of all bits set in the register. For example, if bit 9 (decimal value = 512) and bit 13 (decimal value = 8192) are set, this command will return 8704.
Usage example	STAT:OPER? / 256
Related Commands	*CLS / *STB? / STATus:OPERation:ENABle

### STATus:OPERation:CONDition?
Syntax	STATus:OPERation:CONDition?
Description	This query returns the value of the read-only Operation Status Condition register.
Return	The value returned is the binary-weighted sum of all bits set in the register. For example, if bit 9 (decimal value = 512) and bit 13 (decimal value = 8192) are set, this command will return 8704.
Usage example	STAT:OPER:COND? / 256
Related Commands	STATus:OPERation:ENABle

### STATus:OPERation:ENABle
Syntax	STATus:OPERation:ENABle {<value>} / STATus:OPERation:ENABle?
Description	This command and its query set and read the value of the Operation Status Enable register. The Enable register is a mask for enabling specific bits from the Operation Event register to set the operation summary bit 7 (OPER) of the Status Byte register. This bit is the logical OR of all the Operational Event register bits that are enabled by the Operation Status Enable register.
Return	Query the Operation Status Enable register. The instrument returns a binary-weighted decimal representing the bits set in the enable register.
Parameters	Name	Type	Range	Default
	<value>	NR1	A decimal value which corresponds to the binary-weighted sum of the bits in the register.	0
Usage example	Enable ISUM (bit 13): / STAT:OPER:ENAB 8192
Related Commands	*CLS / *STB? / STATus:OPERation[:EVENt]?

### STATus:OPERation:INSTrument[:EVENt]?
Syntax	STATus:OPERation:INSTrument[:EVENt]?
Description	This query returns the value of the read-only Instrument Operation Status Event register. The bits are latched and reading the register will clear it. The *CLS command can be also used to clear the register.
Return	The value returned is the binary-weighted sum of all bits set in the register. For example, if bit 1 (decimal value = 2) and bit 2 (decimal value = 4) are set, this command will return 6.
Usage example	If bit 2 is set: / STAT:OPER:INST? / 4
Related Commands	*CLS / STATus:PREset

### STATus:OPERation:INSTrument:CONDition?
Syntax	STATus:OPERation:INSTrument:CONDition?
Description	This query returns the value of the read-only Instrument Operation Status Condition register.
Return	The value returned is the binary-weighted sum of all bits set in the register. For example, if bit 1 (decimal value = 2) and bit 2 (decimal value = 4) are set, this command will return 6.
Usage example	If bit 2 is set: / STAT:OPER:INST:COND? / 4
Related Commands	STATus:PREset

### STATus:OPERation:INSTrument:ENABle
Syntax	STATus:OPERation:INSTrument:ENABle {<value>} / STATus:OPERation:INSTrument:ENABle?
Description	Enable bits in the Instrument Operation Status Enable register. The selected bits are then reported to the Operation Status Event register.
Return	Query the Instrument Operation Status Enable register. The instrument returns a binary-weighted decimal representing the bits set in the enable register.
Parameters	Name	Type	Range	Default
	<value>	NR1	A decimal value which corresponds to the binary-weighted sum of the bits in the register.	PREset=0
Usage example	STAT:OPER:INST:ENAB 6
Related Commands	*CLS / STATus:PREset

### STATus:OPERation:INSTrument:ISUMmary[<n>][:EVENt]?
Syntax	STATus:OPERation:INSTrument:ISUMmary[<n>][:EVENt]?
Description	This query returns the value of the read-only Instrument Isummary Operation Status Event register for a specific channel of the instrument represented by numeric value [<n>]. When [<n>] is omitted, the system queries the Instrument Isummary Operation Status Event register of the current channel. The bits are latched and reading the register will clear it. The *CLS command can be also used to clear the register.
Return	The value returned is the binary-weighted sum of all bits set in the register.
Usage example	If bit 8 and bit 10 on the channel 1 are set (256+1024=1280): / STAT:OPER:INST:ISUM1? / 1280
Related Commands	*CLS

### STATus:OPERation:INSTrument:ISUMmary[<n>]:CONDition?
Syntax	STATus:OPERation:INSTrument:ISUMmary[<n>]:CONDition?
Description	This query returns the value of the read-only Instrument Isummary Operation Status Condition register for a specific channel of the instrument represented by numeric value [<n>]. When [<n>] is omitted, the system queries the Instrument Isummary Operation Status Condition register of the current channel.
Return	The value returned is the binary-weighted sum of all bits set in the register.
Usage example	If bit 8 and bit 10 on the channel 1 are set (256+1024=1280): / STAT:OPER:INST:ISUM1:COND? / 1280

### STATus:OPERation:INSTrument:ISUMmary<n>:ENABle
Syntax	STATus:OPERation:INSTrument:ISUMmary[<n>]:ENABle {<value>} / STATus:OPERation:INSTrument:ISUMmary[<n>]:ENABle?
Description	Enable bits in the Instrument Isummary Operation Status Enable register for a specific channel of the instrument represented by numeric value [<n>]. When [<n>] is omitted, the system queries the Instrument Isummary Operation Status Enable register of the current channel. The selected bits are then reported to the Status Byte. / This command and its query set and read the value of the Operation Status Enable register. The Enable register is a mask for enabling specific bits from the Operation Event register to set the operation summary bit (OPER) of the Status Byte register. This bit (bit 7) is the logical OR of all the Operational Event register bits that are enabled by the Operation Status Enable register
Return	Query the Instrument Isummary Operation Status Enable register. The instrument returns a binary-weighted decimal representing the bits set in the enable register.
Parameters	Name	Type	Range	Default
	<value>	NR1	A decimal value which corresponds to the binary-weighted sum of the bits in the register.	0
Usage example	The query returns that bit 0, 1 and 4 are set (1+2+16=19): / STAT:OPER:INST:ISUM:ENABLE? / 19
Related Commands	*CLS / STATus:PREset

### STATus:PREset
Syntax	STATus:PREset
Description	This command clears all bits in the Enable registers.
Return	None
Usage example	STAT:PRE
Related Commands	*CLS

### STATus:QUEStionable[:EVENt]?
Syntax	STATus:QUEStionable[:EVENt]?
Description	Query the Questionable Status event register. The bits are latched and reading the register will clear it. The *CLS command can be also used to clear the register.
Return	The instrument returns a decimal value which corresponds to the binary-weighted sum of all bits in the register.
Usage example	STAT:QUES? / 8
Related Commands	*CLS

### STATus:QUEStionable:CONDition?
Syntax	STATus:QUEStionable:CONDition?
Description	Query the Questionable Status condition register.
Return	The instrument returns a decimal value which corresponds to the binary-weighted sum of all bits in the register.
Usage example	STAT:QUES:COND? / 8

### STATus:QUEStionable:ENABle
Syntax	STATus:QUEStionable:ENABle {<value>} / STATus:QUEStionable:ENABle?
Description	Enable bits in the Questionable Status Enable register. The selected bits are then reported to the Status Byte. / When <enable value> is set to 0, executing this command will clear the Questionable Status Enable register.
Return	Query the Questionable Status Enable register. The instrument returns a binary-weighted decimal representing the bits set in the enable register.
Parameters	Name	Type	Range	Default
	<value>	NR1	A decimal value which corresponds to the binary-weighted sum of the bits in the register.	0
Usage example	The query returns bit 3 4 and 13 are enabled (8+16+8192=8216): / STAT:QUES:ENAB? / 8216
Related Commands	*CLS / STATus:PREset

### STATus:QUEStionable:INSTrument[:EVENt]?
Syntax	STATus:QUEStionable:INSTrument[:EVENt]?
Description	Query the questionable instrument event register. The bits are latched and reading the register will clear it. The *CLS command can be also used to clear the register.
Return	The instrument returns a decimal value which corresponds to the binary-weighted sum of all bits in the register and clears the register.
Usage example	Result of the query when bit 1 and 2 are set (2+4=6): / STAT:QUES:INST? / 6
Related Commands	*CLS

### STATus:QUEStionable:INSTrument:CONDition?
Syntax	STATus:QUEStionable:INSTrument:CONDition?
Description	Query the questionable instrument condition register.
Return	The instrument returns a decimal value which corresponds to the binary-weighted sum of all bits in the register and clears the register.
Usage example	Result of the query when bit 1 and 2 are set (2+4=6): / STAT:QUES:INST:COND? / 6

### STATus:QUEStionable:INSTrument:ENABle
Syntax	STATus:QUEStionable:INSTrument:ENABle {<value>} / STATus:QUEStionable:INSTrument:ENABle?
Description	Set the value of the questionable instrument enable register. This register is a mask for enabling specific bits from the questionable instrument event register to set the instrument summary bit 13 (ISUM) of the Questionable Status register. The ISUM bit of the Questionable Status register is the logical OR of all the questionable instrument event register bits that are enabled by the questionable instrument enable register.
Return	Query the Questionable Instrument Enable register. The instrument returns a binary-weighted decimal representing the bits set in the enable register.
Parameters	Name	Type	Range	Default
	<value>	NR1	A decimal value which corresponds to the binary-weighted sum of the bits in the register	0
Usage example	Set bit 1 and 2: / STAT:QUES:INST:ENAB 6
Related Commands	*CLS

### STATus:QUEStionable:INSTrument:ISUMmary[<n>][:EVENt]?
Syntax	STATus:QUEStionable:INSTrument:ISUMmary[<n>][:EVENt]?
Description	Return the value of the Questionable Instrument Isummary Event register for a specific channel of the instrument represented by numeric value [<n>]. When [<n>] is omitted, the system queries the questionable instrument Isummary enable register of the current channel. The event register is a read-only register which holds (latches) all events. Reading the Questionable Instrument Isummary Event register clears it. The *CLS command can be also used to clear the register.
Return	The instrument returns a binary-weighted decimal representing the bits set in the enable register.
Usage example	STAT:QUES:INST:ISUM1? / 512
Related Commands	*CLS

### STATus:QUEStionable:INSTrument:ISUMmary[<n>]:CONDition?
Syntax	STATus:QUEStionable:INSTrument:ISUMmary[<n>]:CONDition?
Description	Return the value of the Questionable Instrument Isummary Condition register for a specific channel of the instrument represented by numeric value [<n>]. When [<n>] is omitted, the system queries the questionable instrument Isummary enable register of the current channel.
Return	The instrument returns a binary-weighted decimal representing the bits set in the enable register.
Usage example	STAT:QUES:INST:ISUM1:COND? / 512

### STATus:QUEStionable:INSTrument:ISUMmary[<n>]:ENABle
Syntax	STATus:QUEStionable:INSTrument:ISUMmary[<n>]:ENABle {<value>} / STATus:QUEStionable:INSTrument:ISUMmary[<n>]:ENABle?
Description	Set the value of the Questionable Instrument Isummary Enable register for a specific channel of the instrument represented by numeric value [<n>]. When [<n>] is omitted, the system queries the Questionable Instrument Isummary Enable register of the current channel. The *CLS command can be used to clear the register. / This register is a mask for enabling specific bits from the Questionable Instrument Isummary Event register to set the Instrument Summary bit (bits 1 and 2) of the Questionable Instrument register. These bits are the logical OR of all the Questionable Instrument Isummary Event register bits that are enabled by the Questionable Instrument Isummary Enable register.
Return	Query the value of the Questionable Instrument Isummary Enable register.
Parameters	Name	Type	Range	Default
	<value>	NR1	A decimal value which corresponds to the binary-weighted sum of the bits in the register	0
Usage example	STAT:QUES:INST:ISUM2:ENAB 1811
Related Commands	*CLS / STATus:PREset