# SYSTem Commands

SYSTem Commands are the fundamental commands for the operation of an oscilloscope. They can either be used for operational control or screen data interception and more. SYSTem Commands include:
- :RUN
- :STOP
- :AUTO
- :HARDcopy
The detailed information of each command are given as follows:
## :RUN
Command format	:RUN
Function explanation	The command initiates the oscilloscope to acquire waveform data according to its / current settings. Acquisition runs continuously until the oscilloscope receives a :STOP command.

## :STOP
Command format	:STOP
Function explanation	The command controls the oscilloscope to stop acquiring data. To restart the acquisition, use the :RUN command.

## :AUTO
Command format	:AUTO
Function explanation	The command controls the oscilloscope to evaluate all input waveforms characteristics and set the optimum conditions to display the waveforms.

## :HARDcopy
Command format	:HARDcopy
Function explanation	The command controls the oscilloscope to evaluate all input waveforms characteristics and set the optimum conditions to display the waveforms.