# :DECoder Commands

The :DECoder commands are used to execute decoding settings and operations.

Command List:
- :DECoder<n>:MODE
- :DECoder<n>:DISPlay
- :DECoder<n>:FORMat
- :DECoder<n>:POSition
- :DECoder<n>:THREshold:CHANnel1
- :DECoder<n>:THREshold:CHANnel2
- :DECoder<n>:THREshold:CHANnel3
- :DECoder<n>:THREshold:CHANnel4
- :DECoder<n>:THREshold:AUTO
- :DECoder<n>:CONFig:LABel
- :DECoder<n>:CONFig:LINE
- :DECoder<n>:CONFig:FORMat
- :DECoder<n>:CONFig:ENDian
- :DECoder<n>:CONFig:WIDth
- :DECoder<n>:CONFig:SRATe?
- :DECoder<n>:UART (Option)
- :DECoder<n>:IIC (Option)
- :DECoder<n>:SPI (Option)
- :DECoder<n>:PARallel
## :DECoder<n>:MODE
Syntax	:DECoder<n>:MODE <mode> / :DECoder<n>:MODE?
Description	Set or query the decoder type.
Parameter	Name	Type	Range	Default
	<n>	Discrete	{1|2}	--
	<mode>	Discrete	{PARallel|UART|SPI|IIC}	PARallel
Explanation	PARallel, UART, SPI and IIC correspond to parallel decoding, RS232 decoding, SPI decoding and I2C decoding respectively. Wherein, RS232 decoding, SPI decoding and I2C decoding are options and this command is only available when the corresponding option is installed.
Return format	The query returns PAR, UART, SPI or IIC.
Example	:DECoder1:MODE SPI /*Set the decoder type to SPI*/ / :DECoder1:MODE? /*The query returns SPI*/

## :DECoder<n>:DISPlay
Syntax	:DECoder<n>:DISPlay <bool> / :DECoder<n>:DISPlay?
Description	Turn on or off the decoder or query the status of the decoder.
Parameter	Name	Type	Range	Default
	<n>	Discrete	{1|2}	--
	<bool>	Bool	{{1|ON}|{0|OFF}}	0|OFF
Return format	The query returns 1 or 0.
Example	:DECoder1:DISPlay ON /*Tutn on decoder 1*/ / :DECoder1:DISPlay? /*The query returns 1*/

## :DECoder<n>:FORMat
Syntax	:DECoder<n>:FORMat <fmt> / :DECoder<n>:FORMat?
Description	Set or query the bus display format.
Parameter	Name	Type	Range	Default
	<n>	Discrete	{1|2}	--
	<fmt>	Discrete	{HEX|ASCii|DEC|BIN|LINE}	ASCii
Explanation	HEX: hexadecimal; DEC: decimal; BIN: binary / In LINE format, the actual values of the bus are displayed in binary form and the order is consistent with the bus transmission order. This format is only valid for serial buses which include LSB and MSB endian. If MSB endian is selected, LINE format is the same as binary.
Return format	The query returns HEX, ASC, DEC, BIN or LINE.
Example	:DECoder1:FORMat HEX /*Set the bus display format to hexadecimal*/ / :DECoder1:FORMat? /*The query returns HEX*/

## :DECoder<n>:POSition
Syntax	:DECoder<n>:POSition <pos> / :DECoder<n>:POSition?
Description	Set or query the vertical position of the bus on the screen.
Parameter	Name	Type	Range	Default
	<n>	Discrete	{1|2}	--
	<pos>	Integer	50 to 350	350
Explanation	The screen is divided into 400 parts vertically which are marked as 0 to 400 from top to bottom respectively. The range of <pos> is from 50 to 350.
Return format	The query returns an integer between 50 and 350.
Example	:DECoder1:POSition 300 /*Set the vertical position of the bus to 300*/ / :DECoder1:POSition? /*The query returns 300*/

## :DECoder<n>:THREshold:CHANnel1
## :DECoder<n>:THREshold:CHANnel2
## :DECoder<n>:THREshold:CHANnel3
## :DECoder<n>:THREshold:CHANnel4
Syntax	:DECoder<n>:THREshold:CHANnel1 <thre> / :DECoder<n>:THREshold:CHANnel1? / :DECoder<n>:THREshold:CHANnel2 <thre> / :DECoder<n>:THREshold:CHANnel2? / :DECoder<n>:THREshold:CHANnel3 <thre> / :DECoder<n>:THREshold:CHANnel3? / :DECoder<n>:THREshold:CHANnel4 <thre> / :DECoder<n>:THREshold:CHANnel4?
Description	Set or query the threshold level of the specified analog channel.
Parameter	Name	Type	Range	Default
	<n>	Discrete	{1|2}	--
	<thre>	Real	(-4*Vertical Scale –Vertical Offset) to / (4*Vertical Scale – Vertical Offset)	--
Explanation	Vertical Scale is the vertical scale of the specified analog channel. Vertical Offset is the vertical position of the specified analog channel. / By default, the auto threshold function of the analog channels of the oscilloscope is turned on. To set the threshold level manually, send the :DECoder<n>:THREshold:AUTO command to turn off the auto threshold function.
Return format	The query returns the level in scientific notation.
Example	:DECoder1:THREshold:CHANnel4 1.5 /*Set the threshold level of CH4 to 1.5V*/ / :DECoder1:THREshold:CHANnel4? /*The query returns 1.500000e+00*/

## :DECoder<n>:THREshold:AUTO
Syntax	:DECoder<n>:THREshold:AUTO <bool> / :DECoder<n>:THREshold:AUTO?
Description	Turn on or off the auto threshold function of the analog channels, or query the status of the auto threshold function of the analog channels.
Parameter	Name	Type	Range	Default
	<n>	Discrete	{1|2}	--
	<bool>	Bool	{{1|ON}|{0|OFF}}	1|ON
Explanation	By default, the auto threshold function of the analog channels of the oscilloscope is turned on. To set the threshold level manually, send this command to turn off the auto threshold function and use the commands in Related Commands to set the threshold manually.
Return format	The query returns 1 or 0.
Example	:DECoder1:THREshold:AUTO OFF /*Turn off the auto threshold function*/ / :DECoder1:THREshold:AUTO? /*The query returns 0*/
Related commands	:DECoder<n>:THREshold:CHANnel1 / :DECoder<n>:THREshold:CHANnel2 / :DECoder<n>:THREshold:CHANnel3 / :DECoder<n>:THREshold:CHANnel4

## :DECoder<n>:CONFig:LABel
Syntax	:DECoder<n>:CONFig:LABel <bool> / :DECoder<n>:CONFig:LABel?
Description	Turn on or off the label display function, or query the status of the label display function.
Parameter	Name	Type	Range	Default
	<n>	Discrete	{1|2}	--
	<bool>	Bool	{{1|ON}|{0|OFF}}	1|ON
Explanation	When this function is turned on, the bus label will be displayed at the lower-upper side of the bus (when the bus display is turned on).
Return format	The query returns 1 or 0.
Example	:DECoder1:CONFig:LABel ON /*Turn on the label display function*/ / :DECoder1:CONFig:LABel? /*The query returns 1*/

## :DECoder<n>:CONFig:LINE
Syntax	:DECoder<n>:CONFig:LINE <bool> / :DECoder<n>:CONFig:LINE?
Description	Turn on or off the bus display function, or query the status of the bus display function.
Parameter	Name	Type	Range	Default
	<n>	Discrete	{1|2}	--
	<bool>	Bool	{{1|ON}|{0|OFF}}	1|ON
Explanation	When this function is enabled, the bus will be displayed on the screen. You can send the :DECoder<n>:POSition command to adjust the vertical display position of the bus.
Return format	The query returns 1 or 0.
Example	:DECoder1:CONFig:LINE OFF /*Turn off the bus display function*/ / :DECoder1:CONFig:LINE? /*The query returns 0*/

## :DECoder<n>:CONFig:FORMat
Syntax	:DECoder<n>:CONFig:FORMat <bool> / :DECoder<n>:CONFig:FORMat?
Description	Turn on or off the format display function, or query the status of the format display function.
Parameter	Name	Type	Range	Default
	<n>	Discrete	{1|2}	--
	<bool>	Bool	{{1|ON}|{0|OFF}}	1|ON
Explanation	When this function is turned on, the current bus display format will be displayed at the right of the label display (when the bus display is turned on). You can send the :DECoder<n>:FORMat command to set the bus display format.
Return format	The query returns 1 or 0.
Example	:DECoder1:CONFig:FORMat OFF /*Turn off the format display function*/ / :DECoder1:CONFig:FORMat? /*The query returns 0*/

## :DECoder<n>:CONFig:ENDian
Syntax	:DECoder<n>:CONFig:ENDian <bool> / :DECoder<n>:CONFig:ENDian?
Description	Turn on or off the endian display function in serial bus decoding, or query the status of the endian display function in serial bus decoding.
Parameter	Name	Type	Range	Default
	<n>	Discrete	{1|2}	--
	<bool>	Bool	{{1|ON}|{0|OFF}}	0|OFF
Explanation	This command is invalid in parallel decoding. / When this function is enabled, the current bus endian will be displayed at the right of the format display (when the bus display is turned on).
Return format	The query returns 1 or 0.
Example	:DECoder1:CONFig:ENDian ON /*Turn on the endian display function*/ / :DECoder1:CONFig:ENDian? /*The query returns 1*/

## :DECoder<n>:CONFig:WIDth
Syntax	:DECoder<n>:CONFig:WIDth <bool> / :DECoder<n>:CONFig:WIDth?
Description	Turn on or off the width display function, or query the status of the width display function.
Parameter	Name	Type	Range	Default
	<n>	Discrete	{1|2}	--
	<bool>	Bool	{{1|ON}|{0|OFF}}	0|OFF
Explanation	When this function is enabled, the width of each frame of data will be displayed at the right of the endian display (when the bus display is turned on).
Return format	The query returns 1 or 0.
Example	:DECoder1:CONFig:WIDth ON /*Turn on the width display function*/ / :DECoder1:CONFig:WIDth? /*The query returns 1*/

## :DECoder<n>:CONFig:SRATe?
Syntax	:DECoder<n>:CONFig:SRATe?
Description	Query the current digital sample rate.
Parameter	Name	Type	Range	Default
	<n>	Discrete	{1|2}	--
Explanation	The digital sample rate is related to the data source currently selected. By default, the data source is “Trace”; at this point, the digital sample rate is related to the horizontal time base.
Return format	The query returns the digital sample rate in scientific notation.
Example	:DECoder1:CONFig:SRATe? /*The query returns 1.000000e+08*/

# :DECoder<n>:UART (Option)

The :DECoder<n>:UART commands are used to set the RS232 decoding parameters.

Command List:
- :DECoder<n>:UART:TX
- :DECoder<n>:UART:RX
- :DECoder<n>:UART:POLarity
- :DECoder<n>:UART:ENDian
- :DECoder<n>:UART:BAUD
- :DECoder<n>:UART:WIDTh
- :DECoder<n>:UART:STOP
- :DECoder<n>:UART:PARity
## :DECoder<n>:UART:TX
Syntax	:DECoder<n>:UART:TX <tx> / :DECoder<n>:UART:TX?
Description	Set or query the TX channel source of RS232 decoding.
Parameter	Name	Type	Range	Default
	<n>	Discrete	{1|2}	--
	<tx>	Discrete	{D0|D1|D2|D3|D4|D5|D6|D7|D8| / D9|D10|D11|D12|D13|D14|D15| / CHANnel1|CHANnel2|CHANnel3|CHANnel4|OFF}	CHANnel1
Explanation	When OFF is selected, no TX channel source will be set. The TX channel source and RX channel source (:DECoder<n>:UART:RX) cannot be both set to OFF.
Return format	The query returns D0, D1, D2, D3, D4, D5, D6, D7, D8, D9, D10, D11, D12, D13, D14, D15, CHAN1, CHAN2, CHAN3, CHAN4 or OFF.
Example	:DECoder1:UART:TX CHAN2 /*Set the TX channel source to CH2*/ / :DECoder1:UART:TX? /*The query returns CHAN2*/

## :DECoder<n>:UART:RX
Syntax	:DECoder<n>:UART:RX <rx> / :DECoder<n>:UART:RX?
Description	Set or query the RX channel source of RS232 decoding.
Parameter	Name	Type	Range	Default
	<n>	Discrete	{1|2}	--
	<rx>	Discrete	{D0|D1|D2|D3|D4|D5|D6|D7|D8| / D9|D10|D11|D12|D13|D14|D15| / CHANnel1|CHANnel2|CHANnel3|CHANnel4|OFF}	OFF
Explanation	When OFF is selected, no RX channel source will be set. The RX channel source and TX channel source (:DECoder<n>:UART:TX) cannot be both set to OFF.
Return format	The query returns D0, D1, D2, D3, D4, D5, D6, D7, D8, D9, D10, D11, D12, D13, D14, D15, CHAN1, CHAN2, CHAN3, CHAN4 or OFF.
Example	:DECoder1:UART:RX CHAN4 /*Set the RX channel source to CH4*/ / :DECoder1:UART:RX? /*The query returns CHAN4*/

## :DECoder<n>:UART:POLarity
Syntax	:DECoder<n>:UART:POLarity <pol> / :DECoder<n>:UART:POLarity?
Description	Set or query the polarity of RS232 decoding.
Parameter	Name	Type	Range	Default
	<n>	Discrete	{1|2}	--
	<pol>	Discrete	{NEGative|POSitive}	POSitive
Explanation	NEGative: negative polarity (), namely high level is 0 and low level is 1. The RS232 standard uses negative polarity. / POSitive: positive polarity (), namely high level is 1 and low level is 0.
Return format	The query returns NEG or POS.
Example	:DECoder1:UART:POLarity NEGative /*Set the polarity of RS232 decoding to negative*/ / :DECoder1:UART:POLarity? /*The query returns NEG*/

## :DECoder<n>:UART:ENDian
Syntax	:DECoder<n>:UART:ENDian <endian> / :DECoder<n>:UART:ENDian?
Description	Set or query the endian of RS232 decoding.
Parameter	Name	Type	Range	Default
	<n>	Discrete	{1|2}	--
	<endian>	Discrete	{LSB|MSB}	LSB
Return format	The query returns LSB or MSB.
Example	:DECoder1:UART:ENDian MSB /*Set the endian of RS232 decoding to MSB*/ / :DECoder1:UART:ENDian? /*The query returns MSB*/

## :DECoder<n>:UART:BAUD
Syntax	:DECoder<n>:UART:BAUD <baud> / :DECoder<n>:UART:BAUD?
Description	Set or query the buad rate of RS232 decoding. The default unit is bps (baud per second).
Parameter	Name	Type	Range	Default
	<n>	Discrete	{1|2}	--
	<baud>	Integer	110 to 20M	9600
Return format	The query returns the current baud rate in integer.
Example	:DECoder1:UART:BAUD 57600 /*Set the buad rate of RS232 decoding to 57600*/ / :DECoder1:UART:BAUD? /*The query returns 57600*/

## :DECoder<n>:UART:WIDTh
Syntax	:DECoder<n>:UART:WIDTh <wid> / :DECoder<n>:UART:WIDTh?
Description	Set or query the width of each frame of data in RS232 decoding.
Parameter	Name	Type	Range	Default
	<n>	Discrete	{1|2}	--
	<wid>	Integer	5 to 8	8
Return format	The query returns an integer between 5 and 8.
Example	:DECoder1:UART:WIDTh 7 /*Set the data width in RS232 decoding to 7*/ / :DECoder1:UART:WIDTh? /*The query returns 7*/

## :DECoder<n>:UART:STOP
Syntax	:DECoder<n>:UART:STOP <stop> / :DECoder<n>:UART:STOP?
Description	Set or query the stop bit after each frame of data in RS232 decoding.
Parameter	Name	Type	Range	Default
	<n>	Discrete	{1|2}	--
	<stop>	Discrete	{1|1.5|2}	1
Return format	The query returns 1, 1.5 or 2.
Example	:DECoder1:UART:STOP 1.5 /*Set the stop bit in RS232 decoding to 1.5*/ / :DECoder1:UART:STOP? /*The query returns 1.5*/

## :DECoder<n>:UART:PARity
Syntax	:DECoder<n>:UART:PARity <parity> / :DECoder<n>:UART:PARity?
Description	Set or query the even-odd check mode of the data transmission in RS232 decoding.
Parameter	Name	Type	Range	Default
	<n>	Discrete	{1|2}	--
	<parity>	Discrete	{NONE|EVEN|ODD}	NONE
Return format	The query returns NONE, EVEN or ODD.
Example	:DECoder1:UART:PARity ODD /*Set the even-odd check mode in RS232 decoding to odd*/ / :DECoder1:UART:PARity? /*The query returns ODD*/

# :DECoder<n>:IIC (Option)

The :DECoder<n>:IIC commands are used to set the I2C decoding parameters.

Command List:
- :DECoder<n>:IIC:CLK
- :DECoder<n>:IIC:DATA
- :DECoder<n>:IIC:ADDRess
## :DECoder<n>:IIC:CLK
Syntax	:DECoder<n>:IIC:CLK <clk> / :DECoder<n>:IIC:CLK?
Description	Set or query the signal source of the clock channel in I2C decoding.
Parameter	Name	Type	Range	Default
	<n>	Discrete	{1|2}	--
	<clk>	Discrete	{D0|D1|D2|D3|D4|D5|D6|D7|D8| D9|D10|D11|D12|D13|D14|D15| / CHANnel1|CHANnel2|CHANnel3|CHANnel4}	CHANnel1
Return format	The query returns D0, D1, D2, D3, D4, D5, D6, D7, D8, D9, D10, D11, D12, D13, D14, D15, CHAN1, CHAN2, CHAN3 or CHAN4.
Example	:DECoder1:IIC:CLK D0 /*Set the signal source of the clock channel in I2C decoding to D0*/ / :DECoder1:IIC:CLK? /*The query returns D0*/

## :DECoder<n>:IIC:DATA
Syntax	:DECoder<n>:IIC:DATA <dat> / :DECoder<n>:IIC:DATA?
Description	Set or query the signal source of the data channel in I2C decoding.
Parameter	Name	Type	Range	Default
	<n>	Discrete	{1|2}	--
	<dat>	Discrete	{D0|D1|D2|D3|D4|D5|D6|D7|D8| D9|D10|D11|D12|D13|D14|D15| / CHANnel1|CHANnel2|CHANnel3|CHANnel4}	CHANnel2
Return format	The query returns D0, D1, D2, D3, D4, D5, D6, D7, D8, D9, D10, D11, D12, D13, D14, D15, CHAN1, CHAN2, CHAN3 or CHAN4.
Example	:DECoder1:IIC:DATA D1 /*Set the signal source of the data channel in I2C decoding to D1*/ / :DECoder1:IIC:DATA? /*The query returns D1*/

## :DECoder<n>:IIC:ADDRess
Syntax	:DECoder<n>:IIC:ADDRess <addr> / :DECoder<n>:IIC:ADDRess?
Description	Set or query the address mode of I2C decoding.
Parameter	Name	Type	Range	Default
	<n>	Discrete	{1|2}	--
	<addr>	Discrete	{NORMal|RW}	NORMal
Explanation	NORMal: the address bits (:TRIGger:IIC:AWIDth) does not include the R/W bit. / RW: the address bits (:TRIGger:IIC:AWIDth) includes the R/W bit.
Return format	The query returns NORM or RW.
Example	:DECoder1:IIC:ADDRess RW /*Set the address of I2C decoding to include the R/W bit*/ / :DECoder1:IIC:ADDRess? /*The query returns RW*/

# :DECoder<n>:SPI (Option)

The :DECoder<n>:SPI commands are used to set the SPI decoding parameters.

Command List:
- :DECoder<n>:SPI:CLK
- :DECoder<n>:SPI:MISO
- :DECoder<n>:SPI:MOSI
- :DECoder<n>:SPI:CS
- :DECoder<n>:SPI:SELect
- :DECoder<n>:SPI:MODE
- :DECoder<n>:SPI:TIMeout
- :DECoder<n>:SPI:POLarity
- :DECoder<n>:SPI:EDGE
- :DECoder<n>:SPI:ENDian
- :DECoder<n>:SPI:WIDTh
## :DECoder<n>:SPI:CLK
Syntax	:DECoder<n>:SPI:CLK <clk> / :DECoder<n>:SPI:CLK?
Description	Set or query the signal source of the clock channel in SPI decoding.
Parameter	Name	Type	Range	Default
	<n>	Discrete	{1|2}	--
	<clk>	Discrete	{D0|D1|D2|D3|D4|D5|D6|D7|D8| D9|D10|D11|D12|D13|D14|D15| / CHANnel1|CHANnel2|CHANnel3|CHANnel4}	CHANnel1
Return format	The query returns D0, D1, D2, D3, D4, D5, D6, D7, D8, D9, D10, D11, D12, D13, D14, D15, CHAN1, CHAN2, CHAN3 or CHAN4.
Example	:DECoder1:SPI:CLK D0 /*Set the signal source of the clock channel in SPI decoding to D0*/ / :DECoder1:SPI:CLK? /*The query returns D0*/

## :DECoder<n>:SPI:MISO
Syntax	:DECoder<n>:SPI:MISO <miso> / :DECoder<n>:SPI:MISO?
Description	Set or query the MISO channel source in SPI decoding.
Parameter	Name	Type	Range	Default
	<n>	Discrete	{1|2}	--
	<miso>	Discrete	{D0|D1|D2|D3|D4|D5|D6|D7|D8| / D9|D10|D11|D12|D13|D14|D15| / CHANnel1|CHANnel2|CHANnel3|CHANnel4|OFF}	OFF
Explanation	When OFF is selected, no MISO channel source will be set. The MISO channel source and MOSI channel source (:DECoder<n>:SPI:MOSI) cannot be both set to OFF.
Return format	The query returns D0, D1, D2, D3, D4, D5, D6, D7, D8, D9, D10, D11, D12, D13, D14, D15, CHAN1, CHAN2, CHAN3, CHAN4 or OFF.
Example	:DECoder1:SPI:MISO D0 /*Set the MISO channel source in SPI decoding to D0*/ / :DECoder1:SPI:MISO? /*The query returns D0*/

## :DECoder<n>:SPI:MOSI
Syntax	:DECoder<n>:SPI:MOSI <mosi> / :DECoder<n>:SPI:MOSI?
Description	Set or query the MOSI channel source in SPI decoding.
Parameter	Name	Type	Range	Default
	<n>	Discrete	{1|2}	--
	<mosi>	Discrete	{D0|D1|D2|D3|D4|D5|D6|D7|D8| / D9|D10|D11|D12|D13|D14|D15| / CHANnel1|CHANnel2|CHANnel3|CHANnel4|OFF}	CHANnel2
Explanation	When OFF is selected, no MOSI channel source will be set. The MOSI channel source and MISO channel source (:DECoder<n>:SPI:MISO) cannot be both set to OFF.
Return format	The query returns D0, D1, D2, D3, D4, D5, D6, D7, D8, D9, D10, D11, D12, D13, D14, D15, CHAN1, CHAN2, CHAN3, CHAN4 or OFF.
Example	:DECoder1:SPI:MOSI D1 /*Set the MOSI channel source in SPI decoding to D1*/ / :DECoder1:SPI:MOSI? /*The query returns D1*/

## :DECoder<n>:SPI:CS
Syntax	:DECoder<n>:SPI:CS <cs> / :DECoder<n>:SPI:CS?
Description	Set or query the CS channel source in SPI decoding.
Parameter	Name	Type	Range	Default
	<n>	Discrete	{1|2}	--
	<cs>	Discrete	{D0|D1|D2|D3|D4|D5|D6|D7|D8| / D9|D10|D11|D12|D13|D14|D15| / CHANnel1|CHANnel2|CHANnel3|CHANnel4}	CHANnel3
Explanation	This command is only valid in the CS mode (:DECoder<n>:SPI:MODE).
Return format	The query returns D0, D1, D2, D3, D4, D5, D6, D7, D8, D9, D10, D11, D12, D13, D14, D15, CHAN1, CHAN2, CHAN3 or CHAN4.
Example	:DECoder1:SPI:CS CHANnel4 /*Set the CS channel source in SPI decoding to CH4*/ / :DECoder1:SPI:CS? /*The query returns CHAN4*/

## :DECoder<n>:SPI:SELect
Syntax	:DECoder<n>:SPI:SELect <CsNcs> / :DECoder<n>:SPI:SELect?
Description	Set or query the CS polarity in SPI decoding.
Parameter	Name	Type	Range	Default
	<n>	Discrete	{1|2}	--
	<CsNcs>	Discrete	{NCS|CS}	NCS
Explanation	NCS: low level is valid (). The instrument starts transmitting data when the CS is low. / CS: high level is valid (). The instrument starts transmitting data when the CS is high.
Return format	The query returns NCS or CS.
Example	:DECoder1:SPI:SELect CS /*Set the CS polarity to high level is valid*/ / :DECoder1:SPI:SELect? /*The query returns CS*/

## :DECoder<n>:SPI:MODE
Syntax	:DECoder<n>:SPI:MODE <CsTmo> / :DECoder<n>:SPI:MODE?
Description	Set or query the frame synchronization mode of SPI decoding.
Parameter	Name	Type	Range	Default
	<n>	Discrete	{1|2}	--
	<CsTmo>	Discrete	{CS|TIMeout}	TIMeout
Explanation	CS: it contains a chip select line (CS). You can perform frame synchronization according to CS. At this point, you need to send the :DECoder<n>:SPI:CS and :DECoder<n>:SPI:SELect commands to set the CS channel source and polarity. / TIMeout: you can perform frame synchronization according to the timeout time. At this point, you need to send the :DECoder<n>:SPI:TIMeout command to set the timeout time.
Return format	The query returns CS or TIM.
Example	:DECoder1:SPI:MODE CS /*Set the frame synchronization mode of SPI decoding to CS*/ / :DECoder1:SPI:MODE? /*The query returns CS*/

## :DECoder<n>:SPI:TIMeout
Syntax	:DECoder<n>:SPI:TIMeout <tmo> / :DECoder<n>:SPI:TIMeout?
Description	Set or query the timeout time in the timeout mode of SPI decoding. The default unit is s.
Parameter	Name	Type	Range	Default
	<n>	Discrete	{1|2}	--
	<tmo>	Real	Please refer to the Explanation	1.00us
Explanation	The timeout time should be greater than the maximum pulse width of the clock and lower than the idle time between frames. / This command is only valid in the timeout mode (:DECoder<n>:SPI:MODE).
Return format	The query returns the timeout time in scientific notation.
Example	:DECoder1:SPI:TIMeout 0.000005 /*Set the timeout time to 5us*/ / :DECoder1:SPI:TIMeout? /*The query returns 5.000000e-06*/

## :DECoder<n>:SPI:POLarity
Syntax	:DECoder<n>:SPI:POLarity <pol> / :DECoder<n>:SPI:POLarity?
Description	Set or query the polarity of the SDA data line in SPI decoding.
Parameter	Name	Type	Range	Default
	<n>	Discrete	{1|2}	--
	<pol>	Discrete	{NEGative|POSitive}	POSitive
Explanation	NEGative: . The low level is 1. / POSitive: . The high level is 1.
Return format	The query returns NEG or POS.
Example	:DECoder1:SPI:POLarity NEG ative /*Set the polarity of the SDA data line in SPI decoding to negative*/ / :DECoder1:SPI:POLarity? /*The query returns NEG*/

## :DECoder<n>:SPI:EDGE
Syntax	:DECoder<n>:SPI:EDGE <edge> / :DECoder<n>:SPI:EDGE?
Description	Set or query the clock type when the instrument samples the data line in SPI decoding.
Parameter	Name	Type	Range	Default
	<n>	Discrete	{1|2}	--
	<edge>	Discrete	{RISE|FALL}	RISE
Return format	The query returns RISE or FALL.
Example	:DECoder1:SPI:EDGE FALL /*Set the instrument to sample data on the falling edge of the clock in SPI decoding*/ :DECoder1:SPI:EDGE? /*The query returns FALL*/

## :DECoder<n>:SPI:ENDian
Syntax	:DECoder<n>:SPI:ENDian <endian> / :DECoder<n>:SPI:ENDian?
Description	Set or query the endian of the SPI decoding data.
Parameter	Name	Type	Range	Default
	<n>	Discrete	{1|2}	--
	<endian>	Discrete	{LSB|MSB}	MSB
Return format	The query returns LSB or MSB.
Example	:DECoder1:SPI:ENDian MSB /*Set the data endian of the SPI decoding to MSB*/ / :DECoder1:SPI:ENDian? /*The query returns MSB*/

## :DECoder<n>:SPI:WIDTh
Syntax	:DECoder<n>:SPI:WIDTh <wid> / :DECoder<n>:SPI:WIDTh?
Description	Set or query the number of bits of each frame of data in SPI decoding.
Parameter	Name	Type	Range	Default
	<n>	Discrete	{1|2}	--
	<wid>	Integer	8 to 32	8
Return format	The query returns an integer between 8 and 32.
Example	:DECoder1:SPI:WIDTh 16 /*Set the data width in SPI decoding to 16*/ / :DECoder1:SPI:WIDTh? /*The query returns 16*/

# :DECoder<n>:PARallel

The :DECoder<n>:PARallel commands are used to set the parallel decoding parameters.

Command List:
- :DECoder<n>:PARallel:CLK
- :DECoder<n>:PARallel:EDGE
- :DECoder<n>:PARallel:WIDTh
- :DECoder<n>:PARallel:BITX
- :DECoder<n>:PARallel:SOURce
- :DECoder<n>:PARallel:POLarity
- :DECoder<n>:PARallel:NREJect
- :DECoder<n>:PARallel:NRTime
- :DECoder<n>:PARallel:CCOMpensation
- :DECoder<n>:PARallel:PLOT
## :DECoder<n>:PARallel:CLK
Syntax	:DECoder<n>:PARallel:CLK <clk> / :DECoder<n>:PARallel:CLK?
Description	Set or query the CLK channel source of parallel decoding.
Parameter	Name	Type	Range	Default
	<n>	Discrete	{1|2}	--
	<clk>	Discrete	{D0|D1|D2|D3|D4|D5|D6|D7|D8| / D9|D10|D11|D12|D13|D14|D15| / CHANnel1|CHANnel2|CHANnel3|CHANnel4|OFF}	CHANnel1
Return format	The query returns D0, D1, D2, D3, D4, D5, D6, D7, D8, D9, D10, D11, D12, D13, D14, D15, CHAN1, CHAN2, CHAN3, CHAN4 or OFF.
Example	:DECoder1:PARallel:CLK D0 /*Set the CLK channel source of parallel decoding to D0*/ / :DECoder1:PARallel:CLK? /*The query returns D0*/

## :DECoder<n>:PARallel:EDGE
Syntax	:DECoder<n>:PARallel:EDGE <edge> / :DECoder<n>:PARallel:EDGE?
Description	Set or query the edge type of the clock channel when the instrument samples the data channel in parallel decoding.
Parameter	Name	Type	Range	Default
	<n>	Discrete	{1|2}	--
	<edge>	Discrete	{RISE|FALL|BOTH}	RISE
Explanation	If no clock channel is selected (:DECoder<n>:PARallel:CLK), the instrument will sample when the channel data jumps.
Return format	The query returns RISE, FALL or BOTH.
Example	:DECoder1:PARallel:EDGE BOTH /*Set the oscilloscope to sample data on any edge of the clock channel in parallel decoding*/ :DECoder1:PARallel:EDGE? /*The query returns BOTH*/

## :DECoder<n>:PARallel:WIDTh
Syntax	:DECoder<n>:PARallel:WIDTh <wid> / :DECoder<n>:PARallel:WIDTh?
Description	Set or query the data width (namely the number of bits of each frame of data) of the parallel bus.
Parameter	Name	Type	Range	Default
	<n>	Discrete	{1|2}	--
	<wid>	integer	1 to 16	8
Explanation	After setting the data width using this command, send the :DECoder<n>:PARallel:BITX and :DECoder<n>:PARallel:SOURce commands to select each bit and set the channel source for each bit respectively.
Return format	The query returns an integer between 1 and 16.
Example	:DECoder1:PARallel:WIDTh 16 /*Set the data width in parallel decoding to 16*/ / :DECoder1:PARallel:WIDTh? /*The query returns 16*/

## :DECoder<n>:PARallel:BITX
Syntax	:DECoder<n>:PARallel:BITX <bit> / :DECoder<n>:PARallel:BITX?
Description	Set or query the data bit that requires a channel source on the parallel bus.
Parameter	Name	Type	Range	Default
	<n>	Discrete	{1|2}	--
	<bit>	Integer	0 to (data width-1)	0
Explanation	Set the data width using the :DECoder<n>:PARallel:WIDTh command. / After selecting the desired bit, send the :DECoder<n>:PARallel:SOURce command to set the channel source of this bit.
Return format	The query returns the current data bit in integer.
Example	:DECoder1:PARallel:BITX 2 /*Set the current bit to 2*/ / :DECoder1:PARallel:BITX? /*The query returns 2*/

## :DECoder<n>:PARallel:SOURce
Syntax	:DECoder<n>:PARallel:SOURce <src> / :DECoder<n>:PARallel:SOURce?
Description	Set ro query the channel source of the data bit currently selected.
Parameter	Name	Type	Range	Default
	<n>	Discrete	{1|2}	--
	<src>	Discrete	{D0|D1|D2|D3|D4|D5|D6|D7|D8| / D9|D10|D11|D12|D13|D14|D15| / CHANnel1|CHANnel2|CHANnel3|CHANnel4}	Related to the bit selected
Explanation	Before sending this command, use the :DECoder<n>:PARallel:BITX command to select the desired data bit.
Return format	The query returns D0, D1, D2, D3, D4, D5, D6, D7, D8, D9, D10, D11, D12, D13, D14, D15, CHAN1, CHAN2, CHAN3 or CHAN4.
Example	:DECoder1:PARallel:SOURce CHANnel2 /*Set the channel source of the current bit to CH2*/ / :DECoder1:PARallel:SOURce? /*The query returns CHAN2*/
Related command	:DECoder<n>:PARallel:WIDTh

## :DECoder<n>:PARallel:POLarity
Syntax	:DECoder<n>:PARallel:POLarity <pol> / :DECoder<n>:PARallel:POLarity?
Description	Set ro query the data polarity of parallel decoding.
Parameter	Name	Type	Range	Default
	<n>	Discrete	{1|2}	--
	<pol>	Discrete	{NEGative|POSitive}	POSitive
Explanation	NEGative: . The low level is 1. / POSitive: . The high level is 1.
Return format	The query returns NEG or POS.
Example	:DECoder1:PARallel:POLarity NEGative /*Set the data polarity of parallel decoding to negative*/ / :DECoder1:PARallel:POLarity? /*The query returns NEG*/

## :DECoder<n>:PARallel:NREJect
Syntax	:DECoder<n>:PARallel:NREJect <bool> / :DECoder<n>:PARallel:NREJect?
Description	Turn on or off the noise rejection function of parallel decoding, or query the status of the noise rejection function of parallel decoding.
Parameter	Name	Type	Range	Default
	<n>	Discrete	{1|2}	--
	<bool>	Bool	{{1|ON}|{0|OFF}}	0|OFF
Explanation	Noise rejection can remove the data without enough duration on the bus to eliminate the glitches of the actual circuit. / When the noise rejection is turned on, sending the :DECoder<n>:PARallel:NRTime command can set the desired rejection time.
Return format	The query returns 1 or 0.
Example	:DECoder1:PARallel:NREJect ON /*Turn on the noise rejection function*/ / :DECoder1:PARallel:NREJect? /*The query returns 1*/

## :DECoder<n>:PARallel:NRTime
Syntax	:DECoder<n>:PARallel:NRTime <time> / :DECoder<n>:PARallel:NRTime?
Description	Set or query the noise rejection time of parallel decoding. The default unit is s.
Parameter	Name	Type	Range	Default
	<n>	Discrete	{1|2}	--
	<time>	Real	0.00s to 100ms	0.00s
Explanation	Before sending this command, send the :DECoder<n>:PARallel:NREJect command to turn on the noise rejection function.
Return format	The query returns the noise rejection time in scientific notation.
Example	:DECoder1:PARallel:NRTime 0.01 /*Set the noise rejection time to 10ms*/ / :DECoder1:PARallel:NRTime? /*The query returns 1.000000e-02*/

## :DECoder<n>:PARallel:CCOMpensation
Syntax	:DECoder<n>:PARallel:CCOMpensation <comp> / :DECoder<n>:PARallel:CCOMpensation?
Description	Set or query the clock compensation time of parallel decoding. The default unit is s.
Parameter	Name	Type	Range	Default
	<n>	Discrete	{1|2}	--
	<comp>	Real	-100ms to 100ms	0.00s
Explanation	Setting the compensation time can make fine adjustment of the pahse deviation between the clock line and data line. / This command is invalid when the CLK channel source is set to OFF (:DECoder<n>:PARallel:CLK).
Return format	The query returns the compensation time in scientific notation.
Example	:DECoder1:PARallel:CCOMpensation 0.01 /*Set the compensation time to 10ms*/ :DECoder1:PARallel:CCOMpensation? /*The query returns 1.000000e-02*/

## :DECoder<n>:PARallel:PLOT
Syntax	:DECoder<n>:PARallel:PLOT <bool> / :DECoder<n>:PARallel:PLOT?
Description	Turn on or off the curve function of parallel decoding, or query the status of the curve function of parallel decoding.
Parameter	Name	Type	Range	Default
	<n>	Discrete	{1|2}	--
	<bool>	Bool	{{1|ON}|{0|OFF}}	0|OFF
Explanation	When this function is turned on, the variation trend of the bus data is displayed in vector diagram form.
Return format	The query returns 1 or 0.
Example	:DECoder1:PARallel:PLOT ON /*Turn on the curve function*/ / :DECoder1:PARallel:PLOT? /*The query returns 1*/