# :FUNCtion Commands (Option)

The :FUNCtion commands are used to set the waveform recording and playback parameters.

Command List:
- :FUNCtion:WRECord:FEND
- :FUNCtion:WRECord:FMAX?
- :FUNCtion:WRECord:FINTerval
- :FUNCtion:WRECord:PROMpt
- :FUNCtion:WRECord:OPERate
- :FUNCtion:WRECord:ENABle
- :FUNCtion:WREPlay:FSTart
- :FUNCtion:WREPlay:FEND
- :FUNCtion:WREPlay:FMAX?
- :FUNCtion:WREPlay:FINTerval
- :FUNCtion:WREPlay:MODE
- :FUNCtion:WREPlay:DIRection
- :FUNCtion:WREPlay:OPERate
- :FUNCtion:WREPlay:FCURrent
## :FUNCtion:WRECord:FEND
Syntax	:FUNCtion:WRECord:FEND <frame> / :FUNCtion:WRECord:FEND?
Description	Set or query the end frame of waveform recording.
Parameter	Name	Type	Range	Default
	<frame>	Integer	1 to the maximum number of frames can be recorded currently	5000
Explanation	Use the :FUNCtion:WRECord:FMAX? command to query the maximum number of frames can be recorded currently.
Return format	The query returns the current end frame in integer.
Example	:FUNCtion:WRECord:FEND 4096 /*Set the end frame to 4096*/ / :FUNCtion:WRECord:FEND? /*The query returns 4096*/

## :FUNCtion:WRECord:FMAX?
Syntax	:FUNCtion:WRECord:FMAX?
Description	Query the maximum number of frames can be recorded currently.
Explanation	As the capacity of the waveform memory is fixed, the more the number of points each frame of waveform has, the less the number of waveform frames can be recorded. Thus, the maximum number of frames can be recorded currently is decided by the memory depth currently selected. The less the memory depth, the more the number of waveform frames can be recorded.
Return format	The query returns the maximum number of frames can be recorded currently in integer.

## :FUNCtion:WRECord:FINTerval
Syntax	:FUNCtion:WRECord:FINTerval <interval> / :FUNCtion:WRECord:FINTerval?
Description	Set or query the time interval between frames in waveform recording. The default unit is s.
Parameter	Name	Type	Range	Default
	<interval>	Real	100ns to 10s	100ns
Return format	The query returns the time interval currently set in scientific notation.
Example	:FUNCtion:WRECord:FINTerval 0.001 /*Set the time interval to 1ms*/ / :FUNCtion:WRECord:FINTerval? /*The query returns 1.000000e-03*/

## :FUNCtion:WRECord:PROMpt
Syntax	:FUNCtion:WRECord:PROMpt <bool> / :FUNCtion:WRECord:PROMpt?
Description	Turn on or off the sound prompt when the recording finishes, or query the status of the sound prompt when the recording finishes.
Parameter	Name	Type	Range	Default
	<bool>	Bool	{{1|ON}|{0|OFF}}	1|ON
Explanation	When the sound prompt is turned on, the instrument exerts a sound promt when the recording finishes no matter whether the system sound (refer to :SYSTem:BEEPer) is turned on or not.
Return format	The query returns 1 or 0.
Example	:FUNCtion:WRECord:PROMpt 1 /*Turn on the sound prompt when the recording finishes*/ / :FUNCtion:WRECord:PROMpt? /*The query returns 1*/

## :FUNCtion:WRECord:OPERate
Syntax	:FUNCtion:WRECord:OPERate <opt> / :FUNCtion:WRECord:OPERate?
Description	Start or stop the waveform recording, or query the status of the waveform recording.
Parameter	Name	Type	Range	Default
	<opt>	Discrete	{RUN|STOP}	--
Explanation	Before sending this command, send the :FUNCtion:WRECord:ENABle command to turn on the waveform recording function. Otherwise, this command is invalid.
Return format	The query returns RUN or STOP.
Example	:FUNCtion:WRECord:OPERate RUN /*Start the waveform recording*/ / :FUNCtion:WRECord:OPERate? /*The query returns RUN if the recording is in / progress and returns STOP if the recording has already finished*/

## :FUNCtion:WRECord:ENABle
Syntax	:FUNCtion:WRECord:ENABle <bool> / :FUNCtion:WRECord:ENABle?
Description	Turn on or off the waveform recording function, or query the status of the waveform recording function.
Parameter	Name	Type	Range	Default
	<bool>	Bool	{{1|ON}|{0|OFF}}	0|OFF
Explanation	The waveform recording function can only be enabled when the horizontal timebase mode is “YT” and the horizontal timebase is lower than 200ms. / After turning on the waveform recording function, RUN/STOP can be used to start or stop the waveform recording. At this point, you can send the :FUNCtion:WRECord:OPERate command to start the recording.
Return format	The query returns 1 or 0.
Example	:FUNCtion:WRECord:ENABle 1 /*Turn on the waveform recording function*/ / :FUNCtion:WRECord:ENABle? /*The query returns 1*/

## :FUNCtion:WREPlay:FSTart
Syntax	:FUNCtion:WREPlay:FSTart <sta> / :FUNCtion:WREPlay:FSTart?
Description	Set or query the start frame of waveform playback.
Parameter	Name	Type	Range	Default
	<sta>	Integer	1 to the maximum number of frames recorded	1
Explanation	Use the :FUNCtion:WRECord:FEND command to set the maximum number of frames recorded. / The start frame of waveform playback cannot be greater than the end frame of waveform playback (:FUNCtion:WREPlay:FEND). / You can only set the start frame of waveform playback when a waveform is currently recorded. / You cannot set the start frame of waveform playback during the waveform recording or playback process.
Return format	The query returns an integer.
Example	:FUNCtion:WREPlay:FSTart 5 /*Set the start frame of waveform playback to 5*/ / :FUNCtion:WREPlay:FSTart? /*The query returns 5*/

## :FUNCtion:WREPlay:FEND
Syntax	:FUNCtion:WREPlay:FEND <end> / :FUNCtion:WREPlay:FEND?
Description	Set or query the end frame of waveform playback.
Parameter	Name	Type	Range	Default
	<end>	Integer	1 to the maximum number of frames recorded	The maximum number of frames recorded
Explanation	Use the :FUNCtion:WRECord:FEND command to set the maximum number of frames recorded. / The end frame of waveform playback cannot be lower than the start frame of waveform playback (:FUNCtion:WREPlay:FSTart). / You can only set the end frame of waveform playback when a waveform is currently recorded. / You cannot set the end frame of waveform playback during the waveform recording or playback process.
Return format	The query returns an integer.
Example	:FUNCtion:WREPlay:FEND 4096 /*Set the end frame of waveform playback to 4096*/ / :FUNCtion:WREPlay:FEND? /*The query returns 4096*/

## :FUNCtion:WREPlay:FMAX?
Syntax	:FUNCtion:WREPlay:FMAX?
Description	Query theb maximum number of frames can be played, namely the maximum number of frames recorded.
Explanation	Use the :FUNCtion:WRECord:FEND command to set the maximum number of frames recorded.
Return format	The query returns an integer.

## :FUNCtion:WREPlay:FINTerval
Syntax	:FUNCtion:WREPlay:FINTerval <interval> / :FUNCtion:WREPlay:FINTerval?
Description	Set or query the time interval between frames in waveform playback. The default unit is s.
Parameter	Name	Type	Range	Default
	<interval>	Real	100ns to 10s	100ns
Explanation	You can only set the time interval of waveform playback when a waveform is currently recorded. / You cannot set the time interval of waveform playback during the waveform recording or playback process.
Return format	The query returns the current time interval in scientific notation.
Example	:FUNCtion:WREPlay:FINTerval 0.001 /*Set the time interval to 1ms*/ / :FUNCtion:WREPlay:FINTerval? /*The query returns 1.000000e-03*/

## :FUNCtion:WREPlay:MODE
Syntax	:FUNCtion:WREPlay:MODE <mode> / :FUNCtion:WREPlay:MODE?
Description	Set or query the waveform playback mode.
Parameter	Name	Type	Range	Default
	<mode>	Discrete	{REPeat|SINGle}	SINGle
Explanation	REPeat: cycle playback. Play from the start frame to the end frame and then repeat until you stop it manually. / SINGle: single playback. Play from the start frame to the end frame and then stop. / You can only set the waveform playback mode when a waveform is currently recorded. / You cannot set the waveform playback mode during the waveform recording or playback process.
Return format	The query returns REP or SING.
Example	:FUNCtion:WREPlay:MODE REPeat /*Set the waveform playback mode to cycle*/ / :FUNCtion:WREPlay:MODE? /*The query returns REP*/

## :FUNCtion:WREPlay:DIRection
Syntax	:FUNCtion:WREPlay:DIRection <dir> / :FUNCtion:WREPlay:DIRection?
Description	Set or query the waveform playback direction.
Parameter	Name	Type	Range	Default
	<dir>	Discrete	{FORWard|BACKward}	FORWard
Explanation	FORWard: positive direction. Play from the start frame to the end frame. / BACKward: negative direction. Play from the end frame to the start frame. / You can only set the waveform playback direction when a waveform is currently recorded. / You cannot set the waveform playback direction during the waveform recording or playback process.
Return format	The query returns FORW or BACK.
Example	:FUNCtion:WREPlay:DIRection FORWard /*Set the waveform playback direction to forward*/ / :FUNCtion:WREPlay:DIRection? /*The query returns FORW*/

## :FUNCtion:WREPlay:OPERate
Syntax	:FUNCtion:WREPlay:OPERate <opt> / :FUNCtion:WREPlay:OPERate?
Description	Start, pause or stop the waveform playback, or query the status of the waveform playback.
Parameter	Name	Type	Range	Default
	<opt>	Discrete	{PLAY|PAUSe|STOP}	STOP
Explanation	This command is only valid when waveform has already been recorded.
Return format	The query returns PLAY, PAUS or STOP.
Example	:FUNCtion:WREPlay:OPERate PLAY /*Start the waveform playback*/ / :FUNCtion:WREPlay:OPERate? /*The query returns PLAY if the playback is in progress and returns STOP if the playback finishes*/
Related command	:FUNCtion:WRECord:OPERate

## :FUNCtion:WREPlay:FCURrent
Syntax	:FUNCtion:WREPlay:FCURrent <cur> / :FUNCtion:WREPlay:FCURrent?
Description	Set or query the current frame in waveform playback.
Parameter	Name	Type	Range	Default
	<cur>	Integer	1 to the maximum number of frames recorded	The maximum number of frames recorded
Explanation	Use the :FUNCtion:WRECord:FEND command to set the maximum number of frames recorded. / You can only set the current frame of waveform playback when a waveform is currently recorded. / You cannot set the current frame of waveform playback during the waveform recording or playback process.
Return format	The query returns an integer.
Example	:FUNCtion:WREPlay:FCURrent 300 /*Set the current frame in waveform playback to 300*/ / :FUNCtion:WREPlay:FCURrent? /*The query returns 300*/