# IEEE488.2 Common Commands

The IEEE 488.2 standard defines some common commands used for querying the basic information of the instrument or executing the basic operations. These commands usually start with "*" and the keyword of the command is usually 3-character long.

Command List:
- *CLS
- *ESE
- *ESR?
- *IDN?
- *OPC
- *RST
- *SRE
- *STB?
- *TST?
- *WAI
## *CLS
Syntax	*CLS
Description	Clear all the event registers and clear the error queue.

## *ESE
Syntax	*ESE <value> / *ESE?
Description	Set or query the enable register for the standard event status register set.
Parameter	Name	Type	Range	Default
	<value>	Integer	Refer to Explanation	0
Explanation	The bit 1 and bit 6 of the standard event status register are not used and are always treated as 0; therefore, the range of <value> are the decimal numbers corresponding to the binary numbers X0XXXX0X (X is 1 or 0).
Return format	The query returns an integer which equals the sum of the weights of all the bits that have already been set in the register.
Example	*ESE 16 /*Enable the bit 4 (16 in decimal) of the standard event status register*/ *ESE? /*The query returns 16*/

## *ESR?
Syntax	*ESR?
Description	Query and clear the event register for the standard event status register.
Explanation	The bit 1 and bit 6 of the standard event status register are not used and are always treated as 0. The range of the return value are the decimal numbers corresponding to the binary numbers X0XXXX0X (X is 1 or 0).
Return format	The query returns an integer which equals the sum of the weights of all the bits in the register.

## *IDN?
Syntax	*IDN?
Description	Query the ID string of the instrument.
Return format	The query returns the ID string of the instrument, such as / RIGOL TECHNOLOGIES,MSO1104Z,DS1ZA160801111,00.04.01.

## *OPC
Syntax	*OPC / *OPC?
Description	The *OPC command is used to set the Operation Complete bit (bit 0) in the standard event status register to 1 after the current operation is finished. The *OPC? command is used to query whether the current operation is finished.
Return format	The query returns 1 if the current operation is finished; otherwise, returns 0.

## *RST
Syntax	*RST
Description	Restore the instrument to the default state.
Parameter	Name	Type	Range	Default

## *SRE
Syntax	*SRE <value> / *SRE?
Description	Set or query the enable register for the status byte register set.
Parameter	Name	Type	Range	Default
	<value>	Integer	0 to 255	0
Explanation	The bit 0 and bit 1 of the status byte register are not used and are always treated as 0, therefore, the range of <value> are the decimal numbers corresponding to the binary numbers XXXXXX00 (X is 1 or 0).
Return format	The query returns an integer which equals the sum of the weights of all the bits that have already been set in the register.
Example	*SRE 16 /*Enable the bit 4 (16 in decimal) of the status byte register*/ / *SRE? /*The query returns 16*/

## *STB?
Syntax	*STB?
Description	Query the event register for the status byte register. The value of the status byte register is set to 0 after this command is executed.
Explanation	The bit 0 and bit 1 of the status byte register are not used and are always treated as 0. The query returns the decimal numbers corresponding to the binary numbers X0XXXX0X (X is 1 or 0).
Return format	The query returns an integer which equals the sum of the weights of all the bits in the register.

## *TST?
Syntax	*TST?
Description	Perform a self-test and then return the self-test results.
Return format	The query returns a decimal integer.

## *WAI
Syntax	*WAI
Description	Wait for the operation to finish.
Explanation	The subsequent command can only be carried out after the current command has been executed.