# :MATH Commands
The :MATH commands are used to set the operations between the waveforms of multiple channels.

Note:
The operations include the following types.

Analog Operations
Algebraic Operations: A+B, A-B, A×B, A/B Spectrum Operation: FFT
Functional Operations: intg, diff, sqrt, lg, ln, exp, abs

Logic Operations
A&&B, A||B, A^B, !A

Compound Operations
Combination of two operations (inner and outer)

- For logic operations, the waveform data to be operated is compared with the preset threshold and is converted to 0 or 1. Thus, the result will also be 0 or 1.
- For a relatively complicated operation, you can split it into inner and outer layer operations (namely compound operation) according to your need. The inner layer operation (fx) can only be algebraic operation and the outer layer operation can only be algebraic operation or functional operation.

When the outer layer operation is algeriac operation, at least one of source A and source B of the outer layer operation should be set to FX.
When the outer layer operation is functional operation, the source of the outer layer operation can only be set to FX.

Note: For the inner layer operation (fx), you can send the :MATH:OPTion:FX:SOURce1, :MATH:OPTion:FX:SOURce2 and :MATH:OPTion:FX:OPERator commands to set the sources and operator of the inner layer operation. For the outer layer operation, you can send the :MATH:SOURce1, :MATH:SOURce2 and :MATH:OPERatorcommands to set the sources and operator of the outer layer operation.

For operations which need only a single source, only the :MATH:SOURce1 or :MATH:LSOUrce1 command will be used for setting the source.
Command List:
- :MATH:DISPlay
- :MATH:OPERator
- :MATH:SOURce1
- :MATH:SOURce2
- :MATH:LSOUrce1
- :MATH:LSOUrce2
- :MATH:SCALe
- :MATH:OFFSet
- :MATH:INVert
- :MATH:RESet
- :MATH:FFT:WINDow
- :MATH:FFT:SPLit
- :MATH:FFT:UNIT
- :MATH:FFT:HSCale
- :MATH:FFT:HCENter
- :MATH:OPTion:STARt
- :MATH:OPTion:END
- :MATH:OPTion:INVert
- :MATH:OPTion:SENSitivity
- :MATH:OPTion:DIStance
- :MATH:OPTion:ASCale
- :MATH:OPTion:THReshold1
- :MATH:OPTion:THReshold2
- :MATH:OPTion:FX:SOURce1
- :MATH:OPTion:FX:SOURce2
- :MATH:OPTion:FX:OPERator
## :MATH:DISPlay
Syntax	:MATH:DISPlay <bool> / :MATH:DISPlay?
Description	Enable or disable the math operation function or query the math operation status.
Parameter	Name	Type	Range	Default
	<bool>	Bool	{{1|ON}|{0|OFF}}	0|OFF
Return format	The query returns 1 or 0.
Example	:MATH:DISPlay ON /*Enable the math operation function*/ / :MATH:DISPlay? /*The query returns 1*/

## :MATH:OPERator
Syntax	:MATH:OPERator <opt> / :MATH:OPERator?
Description	Set or query the operator of the math operation.
Parameter	Name	Type	Range	Default
	<opt>	Discrete	{ADD|SUBTract|MULTiply|DIVision|AND|OR|XOR| / NOT|FFT|INTG|DIFF|SQRT|LOG|LN|EXP|ABS}	ADD
Explanation	When the parameter in :MATH:SOURce1 and/or :MATH:SOURce2 is FX, this command is used to set the operator of the outer layer operation of compound operation. The range of <opt> is {ADD|SUBTract|MULTiply|DIVision|INTG|DIFF|SQRT|LOG|LN|EXP|ABS}.
Return format	The query returns ADD, SUBT, MULT, DIV, AND, OR, XOR, NOT, FFT, INTG, DIFF, SQRT, LOG, LN, EXP or ABS.
Example	:MATH:OPERator INTG /*Set the operator of the math operation to integration*/ / :MATH:OPERator? /*The query returns INTG*/

## :MATH:SOURce1
Syntax	:MATH:SOURce1 <src> / :MATH:SOURce1?
Description	Set or query the source or source A of analog operation/the outer layer operation of compound operation.
Parameter	Name	Type	Range	Default
	<src>	Discrete	{CHANnel1|CHANnel2|CHANnel3|CHANnel4|FX}	CHANnel1
Explanation	For algebraic operations, this command is used to set source A. / For spectrum operation, only this command is used to set the source. The range of <src> is {CHANnel1|CHANnel2|CHANnel3|CHANnel4}. / For functional operations, only this command is used to set the source. / For compound operations, this command is used to set source A of the outer layer operation when the outer layer operation is algeriac operation and the range of <src> is {CHANnel1|CHANnel2|CHANnel3|CHANnel4}; this command is used to set the source of the outer layer operation when the outer layer operation is functional operation and <src> can only be FX. / Note: When the outer layer operation of compound operation is algebraic operation, at least one of source A and source B of the outer layer operation should be set to FX. / When “FX” is selected, you can send the :MATH:OPTion:FX:SOURce1, :MATH:OPTion:FX:SOURce2 and :MATH:OPTion:FX:OPERator commands to set the sources and operator of the inner layer operation.
Return format	The query returns CHAN1, CHAN2, CHAN3, CHAN4 or FX.
Example	:MATH:SOURce1 CHANnel3 /*Set the source or source A of analog operation/the outer layer operation of compound operation to CH3*/ :MATH:SOURce1? /*The query returns CHAN3*/

## :MATH:SOURce2
Syntax	:MATH:SOURce2 <src> / :MATH:SOURce2?
Description	Set or query source B of analog operation/the outer layer operation of compound operation.
Parameter	Name	Type	Range	Default
	<src>	Discrete	{CHANnel1|CHANnel2|CHANnel3|CHANnel4|FX}	CHANnel1
Explanation	This command is only applicable to analog operations those require two sources (algebraic operations) and compound operations of which the outer layer operations are algebraic operations. / When the outlayer operation of compound operation is algebraic operation, this command is used to set source B of the outer layer operation. / Note: When the outer layer operation of compound operation is algebraic operation, at least one of source A and source B of the outer layer operation should be set to FX. / When “FX” is selected, you can send the :MATH:OPTion:FX:SOURce1, :MATH:OPTion:FX:SOURce2 and :MATH:OPTion:FX:OPERator commands to set the sources and operator of the inner layer operation.
Return format	The query returns CHAN1, CHAN2, CHAN3, CHAN4 or FX.
Example	:MATH:SOURce2 CHANnel3 /*Set source B of analog operation/the outer layer operation of compound operation to CH3*/ :MATH:SOURce2? /*The query returns CHAN3*/

## :MATH:LSOUrce1
Syntax	:MATH:LSOUrce1 <src> / :MATH:LSOUrce1?
Description	Set or query source A of logic operation.
Parameter	Name	Type	Range	Default
	<src>	Discrete	{D0|D1|D2|D3|D4|D5|D6|D7|D8| / D9|D10|D11|D12|D13|D14|D15| / CHANnel1|CHANnel2|CHANnel3|CHANnel4}	D0
Explanation	The logic operations include A&&B, A||B, A^B and !A.
Return format	The query returns D0, D1, D2, D3, D4, D5, D6, D7, D8, D9, D10, D11, D12, D13, D14, D15, CHAN1, CHAN2, CHAN3 or CHAN4.
Example	:MATH:LSOUrce1 D3 /*Set source A of logic operation to D3*/ / :MATH:LSOUrce1? /*The query returns D3*/

## :MATH:LSOUrce2
Syntax	:MATH:LSOUrce2 <src> / :MATH:LSOUrce2?
Description	Set or query source B of logic operation.
Parameter	Name	Type	Range	Default
Explanation	<src>	Discrete	{D0|D1|D2|D3|D4|D5|D6|D7|D8| / D9|D10|D11|D12|D13|D14|D15| / CHANnel1|CHANnel2|CHANnel3|CHANnel4}	D1
Return format	The logic operations include A&&B, A||B, A^B and !A. / This command is only applicable to logic operations that require two signal sources and is used to set source B.
Example	The query returns D0, D1, D2, D3, D4, D5, D6, D7, D8, D9, D10, D11, D12, D13, D14, D15, CHAN1, CHAN2, CHAN3 or CHAN4.
Explanation	:MATH:LSOUrce2 D4 /*Set source B of logic operation to D4*/ / :MATH:LSOUrce2? /*The query returns D4*/

## :MATH:SCALe
Syntax	:MATH:SCALe <scale> / :MATH:SCALe?
Description	Set or query the vertical scale of the operation result. The unit depends on the operator currently selected and the unit of the source.
Parameter	Name	Type	Range	Default
	<scale>	Real	The max range is from 1p to 5T (in 1-2-5 step)	1.00V
Explanation	The range of the vertical scale is related to the operator currently selected and the vertical scale of the source channel. For the integration (intg) and differential (diff) operations, it is also related to the current horizontal timebase.
Return format	The query returns the vertical scale of the operation result in scientific notation.
Example	:MATH:SCALe 2 /*Set the vertical scale to 2V*/ / :MATH:SCALe? /*The query returns 2.000000e+00*/
Related commands	:CHANnel<n>:SCALe / :CHANnel<n>:UNITs / :MATH:OPERator / :TIMebase[:MAIN]:SCALe

## :MATH:OFFSet
Syntax	:MATH:OFFSet <offs> / :MATH:OFFSet?
Description	Set or query the vertical offset of the operation result. The unit depends on the operator currently selected and the unit of the source.
Parameter	Name	Type	Range	Default
	<offs>	Real	Related to the vertical scale of the operation result. / Range: -1000*MathVerticalScale to / 1000*MathVerticalScale Step: MathVerticalScale/50	0.00V
Explanation	MathVerticalScale is the vertical scale of the operation result and can be set by the :MATH:SCALe command.
Return format	The query returns the vertical offset of the operation result in scientific notation.
Example	:MATH:OFFSet 8 /*Set the vertical offset to 8V*/ / :MATH:OFFSet? /*The query returns 8.000000e+00*/
Related commands	:MATH:OPERator / :CHANnel<n>:UNITs

## :MATH:INVert
Syntax	:MATH:INVert <bool> / :MATH:INVert?
Description	Enable or disable the inverted display mode of the operation result, or query the inverted display mode status of the operation result.
Parameter	Name	Type	Range	Default
	<bool>	Bool	{{1|ON}|{0|OFF}}	0|OFF
Explanation	This command is invalid for the FFT operation. / This command has the same function as the :MATH:OPTion:INVert command.
Return format	The query returns 1 or 0.
Example	:MATH:INVert ON /*Enable the inverted display mode*/ / :MATH:INVert? /*The query returns 1*/
Related command	:MATH:OPERator

## :MATH:RESet
Syntax	:MATH:RESet
Description	Sending this command, the instrument adjusts the vertical scale of the operation result to the most proper value according to the current operator and the horizontal timebase of the source.
Related commands	:MATH:OPERator / Commands :MATH:SCALe / :TIMebase[:MAIN]:SCALe

## :MATH:FFT:WINDow
Syntax	:MATH:FFT:WINDow <wnd> / :MATH:FFT:WINDow?
Description	Set or query the window function of the FFT operation.
Parameter	Name	Type	Range	Default
	<wnd>	Discrete	{RECTangle|BLACkman|HANNing|HAMMing| / FLATtop|TRIangle}	RECTangle
Explanation	Spectral leakage can be considerably decreased when a window function is used. / Different window functions are applicable to measure different waveforms. You need to select the window function according to waveform to be measured and its characteristics.
Return format	The query returns RECT, BLAC, HANN, HAMM, FLAT or TRI.
Example	:MATH:FFT:WINDow BLACkman /*Set the window function of the FFT operation to blackman*/ / :MATH:FFT:WINDow? /* The query returns BLACK*/
Related command	:MATH:OPERator

## :MATH:FFT:SPLit
Syntax	:MATH:FFT:SPLit <bool> / :MATH:FFT:SPLit?
Description	Enable or disable the half-screen display mode of the FFT operation, or query the status of the half display mode of the FFT operation.
Parameter	Name	Type	Range	Default
	<bool>	Bool	{{1|ON}|{0|OFF}}	1|ON
Explanation	Enable the half-screen display mode: the source channel and the FFT operation results are displayed separately. The time domain and frequency domain signals are displayed clearly. / Disable the half-screen display mode (full-screen display mode): the source channel and the FFT operation results are displayed in the same window to view the frequency spectrum more clearly and to perform more precise measurement.
Return format	The query returns 1 or 0.
Example	:MATH:FFT:SPLit OFF /*Disable the half-screen display mode*/ / :MATH:FFT:SPLit? /*The query returns 0*/

## :MATH:FFT:UNIT
Syntax	:MATH:FFT:UNIT <unit> / :MATH:FFT:UNIT?
Description	Set or query the vertical unit of the FFT operation result.
Parameter	Name	Type	Range	Default
	<unit>	Discrete	{VRMS|DB}	DB
Explanation	The query returns VRMS or DB.
Return format	:MATH:FFT:UNIT VRMS /*Set the vertical unit of the FFT operation result to Vrms*/ / :MATH:FFT:UNIT? /*The query returns VRMS*/
Example	:MATH:OPERator

## :MATH:FFT:HSCale
Syntax	:MATH:FFT:HSCale <hsc> :MATH:FFT:HSCale?
Description	Set or query the horizontal scale of the FFT operation result. The default unit is Hz
Parameter	Name	Type	Range	Default
	<hsc>	Real	Refer to Explanation	5MHz
Explanation	<hsc> can be set to 1/20, 1/40, 1/100 and 1/200 of the current screen sample rate (current screen sample rate=100/current horizontal timebase). / For example, if the horizontal timebase of the instrument is 1μs, the current screen sample rate is 100/1μs=100MHz. Thus, the horizontal scale can be set to 5MHz, 2.5MHz, 1MHz or 500kHz. / You can view the detailed information of the frequency spectrum by reducing the horizontal scale.
Return format	The query returns the horizontal scale in scientific notation.
Example	:MATH:FFT:HSCale 500000 /*Set the horizontal scale to 500kHz*/ / :MATH:FFT:HSCale? /*The query returns 5.000000e+05*/
Related commands	:MATH:OPERator / :TIMebase[:MAIN]:SCALe

## :MATH:FFT:HCENter
Syntax	:MATH:FFT:HCENter <cent> / :MATH:FFT:HCENter?
Description	Set or query the center frequency of the FFT operation result, namely the frequency relative to the horizontal center of the screen. The default unit is Hz.
Parameter	Name	Type	Range	Default
	<cent>	Real	0 to (current screen sample rate×2/5)	5MHz
Explanation	Current screen sample rate = 100/current horizontal timebase. / Step = horizontal scale of the FFT operation result/50.
Return format	The query returns the current center frequency in scientific notation.
Example	:MATH:FFT:HCENter 10000000 /*Set the center frequency to 10MHz*/ / :MATH:FFT:HCENter? /*The query returns 1.000000e+07*/
Related commands	:MATH:OPERator / :MATH:FFT:HSCale / :TIMebase[:MAIN]:SCALe

## :MATH:OPTion:STARt
Syntax	:MATH:OPTion:STARt <sta> / :MATH:OPTion:STARt?
Description	Set or query the start point of the waveform math operation.
Parameter	Name	Type	Range	Default
	<sta>	Integer	0 to (End point currently set-1)	0
Explanation	This command is invalid for the FFT operation. Sending this command will modify the start points of all the operations (except FFT). / The source selected is equally divided into 1200 parts horizontally, in which the leftmost is 0 and the rightmost is 1199.
Return format	The query returns an integer.
Example	:MATH:OPTion:STARt 50 /*Set the waveform start point to 50*/ / :MATH:OPTion:STARt? /*The query returns 50*/
Related command	:MATH:OPTion:END

## :MATH:OPTion:END
Syntax	:MATH:OPTion:END <end> / :MATH:OPTion:END?
Description	Set or query the end point of the waveform math operation.
Parameter	Name	Type	Range	Default
	<end>	Discrete	(Start point currently set+1) to 1199	1199
Explanation	This command is invalid for the FFT operation. Sending this command will modify the end points of all the operations (except FFT). / The source selected is equally divided into 1200 parts horizontally, in which the leftmost is 0 and the rightmost is 1199.
Return format	The query returns an integer.
Example	:MATH:OPTion:END 200 /*Set the waveform end point to 200*/ / :MATH:OPTion:END? /*The query returns 200*/
Related command	:MATH:OPTion:STARt

## :MATH:OPTion:INVert
Syntax	:MATH:OPTion:INVert <bool> / :MATH:OPTion:INVert?
Description	Enable or disable the inverted display mode of the operation result, or query the inverted display mode status of the operation result.
Parameter	Name	Type	Range	Default
	<bool>	Bool	{{1|ON}|{0|OFF}}	0|OFF
Explanation	This command is invalid for the FFT operation. Sending this command will modify the inverted display mode status of all the operations (except FFT). / This command has the same function as the :MATH:INVert command.
Return format	The query returns 1 or 0.
Example	:MATH:OPTion:INVert ON /*Enable the inverted display mode*/ / :MATH:OPTion:INVert? /*The query returns 1*/

## :MATH:OPTion:SENSitivity
Syntax	:MATH:OPTion:SENSitivity <sens> / :MATH:OPTion:SENSitivity?
Description	Set or query the sensitivity of the logic operation. The default unit is div (namely the current vertical scale).
Parameter	Name	Type	Range	Default
	<sens>	Real	0 to 0.96div, the step is 0.08div	0
Explanation	This command is only applicable to logic operations (A&&B, A||B, A^B and !A).
Return format	The query returns the sensitivity in scientific notation.
Example	:MATH:OPTion:SENSitivity 0.24 /*Set the sensitivity to 0.24div*/ / :MATH:OPTion:SENSitivity? /*The query returns 2.400000e-01*/
Related commands	:CHANnel<n>:SCALe / :MATH:OPERator

## :MATH:OPTion:DIStance
Syntax	:MATH:OPTion:DIStance <dist> / :MATH:OPTion:DIStance?
Description	Set or query the smoothing window width of differential operation (diff).
Parameter	Name	Type	Range	Default
	<dist>	Integer	3 to 201	3
Explanation	This command is only applicable to differential operation (diff).
Return format	The query returns an integer between 3 and 201.
Example	:MATH:OPTion:DIStance 25 /*Set the smoothing window width to 25*/ / :MATH:OPTion:DIStance? /*The query returns 25*/
Related command	:MATH:OPERator

## :MATH:OPTion:ASCale
Syntax	:MATH:OPTion:ASCale <bool> / :MATH:OPTion:ASCale?
Description	Enable or disable the auto scale setting of the operation result or query the status of the auto scale setting.
Parameter	Name	Type	Range	Default
	<bool>	Bool	{{1|ON}|{0|OFF}}	0|OFF
Explanation	When the auto scale is enabled, the instrument will automatically calculate the vertical scale range according to the current operator, the vertical scale and the horizontal timebase. If the current scale is out of the range, it will adjust the vertical scale to the best value automatically. / Sending this command will modify the auto scale status of all the operation results.
Return format	The query returns 1 or 0.
Example	:MATH:OPTion:ASCale ON /*Enable the auto scale setting */ / :MATH:OPTion:ASCale? /*The query returns 1*/

## :MATH:OPTion:THReshold1
Syntax	:MATH:OPTion:THReshold1 <thre> / :MATH:OPTion:THReshold1?
Description	Set or query the threshold level of source A in logic operations. The default unit is V.
Parameter	Name	Type	Range	Default
	<thre>	Real	(-4*Vertical Scale – Vertical Offset) to (4*Vertical Scale – Vertical Offset)	0.00V
Explanation	This command is only applicable to A&&B, A||B, A^B and !A logic operations of which source A is an analog channel. / Vertical Scale refers to the vertical scale of source A / Vertical Offset refers to the vertical offset of source A / The step is Vertical Scale/25
Return format	The query returns the threshold level in scientific notation.
Example	:MATH:OPTion:THReshold1 0.8 /*Set the threshold level to 800mV*/ / :MATH:OPTion:THReshold1? /*The query returns 8.000000e-01*/
Related commands	:CHANnel<n>:SCALe / :CHANnel<n>:OFFSet / :MATH:LSOUrce1

## :MATH:OPTion:THReshold2
Syntax	:MATH:OPTion:THReshold2 <thre> / :MATH:OPTion:THReshold2?
Description	Set or query the threshold level of source B in logic operations. The default unit is V.
Parameter	Name	Type	Range	Default
	<thre>	Real	(-4*Vertical Scale–Vertical Offset) to (4*Vertical Scale–Vertical Offset)	0.00V
Explanation	This command is only applicable to A&&B, A||B and A^B logic operations of which source B is an analog channel. / Vertical Scale refers to the vertical scale of source B / Vertical Offset refers to the vertical offset of source B / The step is Vertical Scale/25
Return format	The query returns the threshold level in scientific notation.
Example	:MATH:OPTion:THReshold2 0.5 /*Set the threshold level to 0.5V*/ / :MATH:OPTion:THReshold2? /*The query returns 5.000000e-01*/
Related commands	:CHANnel<n>:SCALe / :CHANnel<n>:OFFSet / :MATH:LSOUrce2

## :MATH:OPTion:FX:SOURce1
Syntax	:MATH:OPTion:FX:SOURce1 <src> / :MATH:OPTion:FX:SOURce1?
Description	Set or query source A of the inner layer operation of compound operation.
Parameter	Name	Type	Range	Default
	<src>	Discrete	{CHANnel1|CHANnel2|CHANnel3|CHANnel4}	CHANnel1
Return format	The query returns CHAN1, CHAN2, CHAN3 or CHAN4.
Example	:MATH:OPTion:FX:SOURce1 CHANnel1 /*Set source A of the inner layer operation of compound operation to CH1*/ / :MATH:OPTion:FX:SOURce1? /*The query returns CHAN1*/

## :MATH:OPTion:FX:SOURce2
Syntax	:MATH:OPTion:FX:SOURce2 <src> / :MATH:OPTion:FX:SOURce2?
Description	Set or query source B of the inner layer operation of compound operation.
Parameter	Name	Type	Range	Default
	<src>	Discrete	{CHANnel1|CHANnel2|CHANnel3|CHANnel4}	CHANnel1
Return format	The query returns CHAN1, CHAN2, CHAN3 or CHAN4.
Example	:MATH:OPTion:FX:SOURce2 CHANnel1 /*Set source B of the inner layer operation of compound operation to CH1*/ / :MATH:OPTion:FX:SOURce2? /*The query returns CHAN1*/

## :MATH:OPTion:FX:OPERator
Syntax	:MATH:OPTion:FX:OPERator <op> / :MATH:OPTion:FX:OPERator?
Description	Set or query the operator of the inner layer operation of compound operation.
Parameter	Name	Type	Range	Default
	<op>	Discrete	{ADD|SUBTract|MULTiply|DIVision}	ADD
Return format	The query returns ADD, SUBT, MULT or DIV.
Example	:MATH:OPTion:FX:OPERator ADD /*Set the operator of the inner layer operation of compound operation to addition*/ :MATH:OPTion:FX:OPERator? /*The query returns ADD*/