# :REFerence Commands

The :REFerence commands are used to set the reference waveform parameters.

Command List:
- :REFerence:DISPlay
- :REFerence<n>:ENABle
- :REFerence<n>:SOURce
- :REFerence<n>:VSCale
- :REFerence<n>:VOFFset
- :REFerence<n>:RESet
- :REFerence<n>:CURRent
- :REFerence<n>:SAVe
- :REFerence<n>:COLor
## :REFerence:DISPlay
Syntax	:REFerence:DISPlay <bool> / :REFerence:DISPlay?
Description	Enable or disable the REF function, or query the status of the REF function.
Parameter	Name	Type	Range	Default
	<bool>	Bool	{{1|ON}|{0|OFF}}	0|OFF
Return format	The query returns 1 or 0.
Example	:REFerence:DISPlay ON /*Enable the REF function*/ / :REFerence:DISPlay? /*The query returns 1*/

## :REFerence<n>:ENABle
Syntax	:REFerence<n>:ENABle <bool> / :REFerence<n>:ENABle?
Description	Enable or disable the specified reference channel, or query the status of the specified reference channel.
Parameter	Name	Type	Range	Default
	<n>	Discrete	{1|2|3|4|5|6|7|8|9|10}	1
	<bool>	Bool	{{1|ON}|{0|OFF}}	Ref1: 1|ON / Others: 0|OFF
Return format	The query returns 1 or 0.
Example	:REFerence1:ENABle ON /*Enable reference channel 1*/ / :REFerence1:ENABle? /*The query returns 1*/

## :REFerence<n>:SOURce
Syntax	:REFerence<n>:SOURce <source> / :REFerence<n>:SOURce?
Description	Set or query the source of the current reference channel.
Parameter	Name	Type	Range	Default
	<n>	Discrete	{1|2|3|4|5|6|7|8|9|10}	--
	<source>	Discrete	{D0|D1|D2|D3|D4|D5|D6|D7|D8|D9|D10| / D11|D12|D13|D14|D15|CHANnel1| / CHANnel2|CHANnel3|CHANnel4|MATH}	CHANnel1
Explanation	Only channels currently enabled can be selected as the source of the current reference channel.
Return format	The query returns D0, D1, D2, D3, D4, D5, D6, D7, D8, D9, D10, D11, D12, D13, D14, D15, CHAN1, CHAN2, CHAN3, CHAN4 or MATH.
Example	:REFerence1:SOURce CHANnel1 /*Set the source of reference channel 1 to CH1*/ :REFerence1:SOURce? /*The query returns CHAN1*/

## :REFerence<n>:VSCale
Syntax	:REFerence<n>:VSCale <scale> / :REFerence<n>:VSCale?
Description	Set or query the vertical scale of the specified reference channel. The unit is the same as the unit of the source.
Parameter	Name	Type	Range	Default
	<n>	Discrete	{1|2|3|4|5|6|7|8|9|10}	--
	<scale>	Real	Related to the probe ratio / When probe ratio is 1X: 1mV to 10V / When probe ratio is 10X: 10mV to 100V	100mV
Explanation	This command is valid only when the specified reference channel has stored reference waveform. Otherwise, “No reference data!” will be displayed when sending this command.
Return format	The query returns the vertical scale in scientific notation.
Example	:REFerence1:VSCale 2 /*Set the vertical scale of reference channel 1 to 2V*/ / :REFerence1:VSCale? /*The query returns 2.000000e+00*/
Related commands	:REFerence<n>:SOURce / :CHANnel<n>:PROBe

## :REFerence<n>:VOFFset
Syntax	:REFerence<n>:VOFFset <offset> / :REFerence<n>:VOFFset?
Description	Set or query the vertical offset of the specified reference channel. The unit is the same as the unit of the source.
Parameter	Name	Type	Range	Default
	<n>	Discrete	{1|2|3|4|5|6|7|8|9|10}	--
	<offset>	Real	-10*RefVerticalScale to 10*RefVerticalScale	0
Explanation	RefVerticalScale refers to the vertical scale of the reference channel.
Return format	The query returns the vertical offset in scientific notation.
Example	:REFerence1:VOFFset 0.5 /*Set the vertical offset of reference channel 1 to 500mV*/ / :REFerence1:VOFFset? /*The query returns 5.000000e-01*/
Related commands	:REFerence<n>:SOURce / :REFerence<n>:VSCale

## :REFerence<n>:RESet
Syntax	:REFerence<n>:RESet
Description	Reset the vertical scale and vertical offset of the specified reference channel to their default values.
Parameter	Name	Type	Range	Default
	<n>	Discrete	{1|2|3|4|5|6|7|8|9|10}	--

## :REFerence<n>:CURRent
Syntax	:REFerence<n>:CURRent
Description	Select the current reference channel.
Parameter	Name	Type	Range	Default
	<n>	Discrete	{1|2|3|4|5|6|7|8|9|10}	1
Explanation	Only reference channels currently turned on can be selected as the current reference channel.
Related command	:REFerence<n>:ENABle

## :REFerence<n>:SAVe
Syntax	:REFerence<n>:SAVe
Description	Store the waveform of the current reference channel to the internal memory as reference waveform.
Parameter	Name	Type	Range	Default
	<n>	Discrete	{1|2|3|4|5|6|7|8|9|10}	--
Related command	:REFerence<n>:CURRent

## :REFerence<n>:COLor
Syntax	:REFerence<n>:COLor <color> / :REFerence<n>:COLor?
Description	Set or query the display color of the current reference channel.
Parameter	Name	Type	Range	Default
	<n>	Discrete	{1|2|3|4|5|6|7|8|9|10}	--
	<color>	Discrete	{GRAY|GREEn|DARKgreen|MAGenta|ORANge}	GRAY
Return format	The query returns GRAY, GREE, DARK, MAG or ORAN.
Example	:REFerence1:COLor GREEn /*Set the display color of reference channel 1 (the current reference channel) to GREEn*/ :REFerence1:COLor? /*The query returns GREE*/
Related commands	:REFerence<n>:CURRent