# :SOURce Commands (Only for MSO1000Z-S/DS1000Z-S)

The [:SOURce[<n>]] commands are used to set the parameters of the built-in signal source. <n> can be 1 or 2 which denotes the corresponding built-in signal source channel. When <n> or :SOURce[<n>] is omitted, the operation will be applied to source 1 by default.

Command List:
- [:SOURce[<n>]]:OUTPut[<n>][:STATe]
- [:SOURce[<n>]]:OUTPut[<n>]:IMPedance
- [:SOURce[<n>]]:FREQuency[:FIXed]
- [:SOURce[<n>]]:PHASe[:ADJust]
- [:SOURce[<n>]]:PHASe:INITiate
- [:SOURce[<n>]]:FUNCtion[:SHAPe]
- [:SOURce[<n>]]:FUNCtion:RAMP:SYMMetry
- [:SOURce[<n>]]:VOLTage[:LEVel][:IMMediate][:AMPLitude]
- [:SOURce[<n>]]:VOLTage[:LEVel][:IMMediate]:OFFSet
- [:SOURce[<n>]]:PULSe:DCYCle
- [:SOURce[<n>]]:MOD[:STATe]
- [:SOURce[<n>]]:MOD:TYPe
- [:SOURce[<n>]]:MOD:AM[:DEPTh]
- [:SOURce[<n>]]:MOD:AM:INTernal:FREQuency
- [:SOURce[<n>]]:MOD:FM:INTernal:FREQuency
- [:SOURce[<n>]]:MOD:AM:INTernal:FUNCtion
- [:SOURce[<n>]]:MOD:FM:INTernal:FUNCtion
- [:SOURce[<n>]]:MOD:FM[:DEVIation]
- [:SOURce[<n>]]:APPLy?
- [:SOURce[<n>]]:APPLy:NOISe
- [:SOURce[<n>]]:APPLy:PULSe
- [:SOURce[<n>]]:APPLy:RAMP
- [:SOURce[<n>]]:APPLy:SINusoid
- [:SOURce[<n>]]:APPLy:SQUare
- [:SOURce[<n>]]:APPLy:USER
## [:SOURce[<n>]]:OUTPut[<n>][:STATe]
Syntax	[:SOURce[<n>]]:OUTPut[<n>][:STATe] <bool> / [:SOURce[<n>]]:OUTPut[<n>][:STATe]?
Description	Turn on or off the output of the specified source channel, or query the status of the output of the specified source channel.
Parameter	Name	Type	Range	Default
	[<n>]	Discrete	{1|2}	If omitted, the operation is performed on source 1 by default
	<bool>	Bool	{{1|ON}|{0|OFF}}	0|OFF
Explanation	[:SOURce[<n>]] and :OUTPut [<n>] are used to specify the source channel. The former enjoys higher priority over the latter; namely if the former is omitted, the channel is specified by the latter and if the former is not omitted, the channel is specified by the former.
Return format	The query returns OFF or ON.
Example	:OUTPut 1 /*Turn on the output of source 1*/ / :OUTPut? /*The query returns ON*/

## [:SOURce[<n>]]:OUTPut[<n>]:IMPedance
Syntax	[:SOURce[<n>]]:OUTPut[<n>]:IMPedance <impedance> / [:SOURce[<n>]]:OUTPut[<n>]:IMPedance?
Description	Set or query the impedance of the specified source channel.
Parameter	Name	Type	Range	Default
	[<n>]	Discrete	{1|2}	If omitted, the operation is performed on source 1 by default
	<impedance>	Discrete	{OMEG|FIFTy}	OMEG
Explanation	[:SOURce[<n>]] and :OUTPut [<n>] are used to specify the source channel. The former enjoys higher priority over the latter, namely if the former is omitted, the channel is specified by the latter and if the former is not omitted, the channel is specified by the former. / OMEG: highZ; FIFTy: 50Ω
Return format	The query returns OMEG or FIFT.
Example	:OUTPut:IMPedance FIFTy /*Set the output impedance of source 1 to 50Ω*/ / :OUTPut:IMPedance? /*The query returns FIFT*/

## [:SOURce[<n>]]:FREQuency[:FIXed]
Syntax	[:SOURce[<n>]]:FREQuency[:FIXed] <frequency> / [:SOURce[<n>]]:FREQuency[:FIXed]?
Description	Set or query the output frequency of the specified source channel if the modulation is not enabled or the carrier frequency if the modulation is enabled. The default unit is Hz.
Parameter	Name	Type	Range	Default
	[<n>]	Discrete	{1|2}	If omitted, the operation is performed on source 1 by default
	<frequency>	Real	Sine: 0.1Hz to 25MHz / Square: 0.1Hz to 15MHz / Pulse: 0.1Hz to 1MHz / Ramp: 0.1Hz to 100kHz / Arbitrary waveform: 0.1Hz to / 10MHz	1kHz
Explanation	The query returns the frequency in scientific notation, such as 2.0000000e+05.
Return format	:FREQuency 1000 /*Set the output frequency of source 1 to 1kHz*/ / :FREQuency? /*The query returns 1.0000000e+03*/
Related commands	[:SOURce[<n>]]:MOD[:STATe] / [:SOURce[<n>]]:MOD:TYPe

## [:SOURce[<n>]]:PHASe[:ADJust]
Syntax	[:SOURce[<n>]]:PHASe[:ADJust] <phase> / [:SOURce[<n>]]:PHASe[:ADJust]?
Description	Set or query the start phase of the specified source channel. The default unit is degree (°).
Parameter	Name	Type	Range	Default
	[<n>]	Discrete	{1|2}	If omitted, the operation is performed on source 1 by default
	<phase>	Real	to 360	0
Return format	The query returns the start phase in scientific notation, such as 0.0000000e+00.
Example	:PHASe 90 /*Set the start phase of source 1 to 90°*/ / :PHASe? /*The query returns 9.0000000e+01*/

## [:SOURce[<n>]]:PHASe:INITiate
Syntax	[:SOURce[<n>]]:PHASe:INITiate
Description	Execute the align phase operation.
Parameter	Name	Type	Range	Default
	[<n>]	Discrete	{1|2}	If omitted, the operation is performed on source 1 by default
Explanation	When the align phase operation is performed, the instrument re-configures the two channels to make them output with the specified frequency and phase. / For two signals whose frequencies are the same or in multiple, this operation will align their phases. For example, assume Source1 output a 1kHz, 5Vpp, 0° sine waveform and Source2 outputs a 1kHz, 5Vpp, 180° sine waveform. Sample the two waveforms using another oscilloscope and display them stably; you will see that the waveforms shown on the oscilloscope do not always have a phase deviation of 180°. At this point, execute the align phase operation and the waveforms shown on the oscilloscope will have a phase deviation of 180° without any manual adjustment of the start phase of the generator.

## [:SOURce[<n>]]:FUNCtion[:SHAPe]
Syntax	[:SOURce[<n>]]:FUNCtion[:SHAPe] <wave> / [:SOURce[<n>]]:FUNCtion[:SHAPe]?
Description	Select or query the output waveform when the modulation of the specified source channel is not enabled. Select or query the carrier waveform when the modulation is enabled. At this point, if PULSe, NOISe or DC is selected, the modulation will turn off automatically.
Parameter	Name	Type	Range	Default
	[<n>]	Discrete	{1|2}	If omitted, the operation is performed on source 1 by default
	<wave>	Discrete	{SINusoid|SQUare|RAMP|PULSe| / NOISe|DC|EXTernal||SINC|EXPRise| EXPFall|ECG|GAUSs|LORentz| / HAVersine}	SINusoid
Explanation	EXTernal: arbitrary waveform / MSO1000Z/DS1000Z provides 7 built-in waveforms: Sinc, Exp.Rise, Exp.Fall, ECG, Gauss, Lorentz and Haversine
Return format	The query returns SIN, SQU, RAMP, PULS, NOIS, DC, EXT, SINC, EXPR, EXPF, ECG, GAUS, LOR or HAV.
Syntax	:FUNCtion SQUare /*Set the output waveform of source 1 to square*/ / :FUNCtion? /*The query returns SQU*/

## [:SOURce[<n>]]:FUNCtion:RAMP:SYMMetry
Syntax	[:SOURce[<n>]]:FUNCtion:RAMP:SYMMetry <val> [:SOURce[<n>]]:FUNCtion:RAMP:SYMMetry?
Description	Set or query the ramp symmetry (the percentage that the rising period takes up in the whole period) of the specified source channel.
Parameter	Name	Type	Range	Default
	[<n>]	Discrete	{1|2}	If omitted, the operation is performed on source 1 by default
	<val>	Real	0 to 100	10
Return format	The query returns the symmetry in scientific notation, such as 5.000000e+01.
Example	:FUNCtion:RAMP:SYMMetry 50 /*Set the ramp symmetry of source 1 to 50%*/ / :FUNCtion:RAMP:SYMMetry? /*The query returns 5.000000e+01*/
Related command	[:SOURce[<n>]]:FUNCtion[:SHAPe]

## [:SOURce[<n>]]:VOLTage[:LEVel][:IMMediate][:AMPLitude]
Syntax	[:SOURce[<n>]]:VOLTage[:LEVel][:IMMediate][:AMPLitude] <Amplitude> / [:SOURce[<n>]]:VOLTage[:LEVel][:IMMediate][:AMPLitude]?
Description	Set or query the output amplitude of the specified source channel. The default unit is Vpp.
Parameter	Name	Type	Range	Default
	[<n>]	Discrete	{1|2}	If omitted, the operation is performed on source 1 by default
	<Ampliude>	Real	Related to the output impedance / HighZ: 20mVpp to 5Vpp / 50Ω: 10mVpp to 2.5Vpp	5Vpp
Explanation	You can use the [:SOURce[<n>]]:OUTPut[<n>]:IMPedance command to set the output impedance.
Return format	The query returns the amplitude in scientific notation, such as 1.0000000e+00.
Example	:VOLTage 2 /*Set the output amplitude of source 1 to 2V*/ / :VOLTage? /*The query returns 2.000000e+00*/

## [:SOURce[<n>]]:VOLTage[:LEVel][:IMMediate]:OFFSet
Syntax	[:SOURce[<n>]]:VOLTage[:LEVel] [:IMMediate]:OFFSet <offset> / [:SOURce[<n>]]:VOLTage[:LEVel] [:IMMediate]:OFFSet?
Description	Set or query the DC offset of the specified source channel. The default unit is VDC.
Parameter	Name	Type	Range	Default
	[<n>]	Discrete	{1|2}	If omitted, the operation is performed on source 1 by default
	<offset>	Real	Related to the output impedance and amplitude / HighZ: ±(2.5V-current amplitude/2) / 50Ω: ±(1.25V-current amplitude/2)	0μVDC
Explanation	You can use the [:SOURce[<n>]]:OUTPut[<n>]:IMPedance command to set the output impedance. / You can use the [:SOURce[<n>]]:VOLTage[:LEVel][:IMMediate][:AMPLitude] command to set the output amplitude.
Return format	The query returns the DC offset in scientific notation, such as 1.0000000e+00.
Example	:VOLTage:OFFSet 0.5 /*Set the DC offset of source 1 to 500mVDC*/ / :VOLTage:OFFSet? /*The query returns 5.000000e-01*/

## [:SOURce[<n>]]:PULSe:DCYCle
Syntax	[:SOURce[<n>]]:PULSe:DCYCle <percent> / [:SOURce[<n>]]:PULSe:DCYCle?
Description	Set or query the pulse duty cycle (the percentage that the high level takes up in the whole period) of the specified source channel.
Parameter	Name	Type	Range	Default
	[<n>]	Discrete	{1|2}	If omitted, the operation is performed on source 1 by default
	<percent>	Real	10 to 90	20
Return format	The query returns the duty cycle in scientific notation, such as 5.000000e+01.
Example	:PULSe:DCYCle 50 /*Set the pulse duty cycle of source 1 to 50%*/ :PULSe:DCYCle? /*The query returns 5.000000e+01*/
Related command	[:SOURce[<n>]]:FUNCtion[:SHAPe]

## [:SOURce[<n>]]:MOD[:STATe]
Syntax	[:SOURce[<n>]]:MOD[:STATe] <bool> / [:SOURce[<n>]]:MOD[:STATe]?
Description	Enable or disable the modulation of the specified source channel, or query the status of the modulation of the specified source channel.
Parameter	Name	Type	Range	Default
	[<n>]	Discrete	{1|2}	If omitted, the operation is performed on source 1 by default
	<bool>	Bool	{{1|ON}|{0|OFF}}	0|OFF
Explanation	The signal source of MSO1000Z/DS1000Z provides amplitude modulation (AM) and frequency modulation (FM) which can be selected by sending the [:SOURce[<n>]]:MOD:TYPe command. / Sine, Square, Ramp, Built-in waveforms or Arb waveform (except DC) can be used as the carrier waveform. / You can use the [:SOURce[<n>]]:MOD:AM:INTernal:FUNCtion or [:SOURce[<n>]]:MOD:FM:INTernal:FUNCtion command to selelct Sine, Square, Triangle or Noise as the modulating waveform.
Return format	The query returns OFF or ON.
Syntax	:MOD ON /*Enable the modulation of source 1*/ / :MOD? /*The query returns ON*/
Related command	[:SOURce[<n>]]:FUNCtion[:SHAPe]

## [:SOURce[<n>]]:MOD:TYPe
Syntax	[:SOURce[<n>]]:MOD:TYPe <type> / [:SOURce[<n>]]:MOD:TYPe?
Description	Set or query the modulation type of the specified source channel.
Parameter	Name	Type	Range	Default
	[<n>]	Discrete	{1|2}	If omitted, the operation is performed on source 1 by default
	<type>	Discrete	{AM|FM}	AM
Explanation	AM: amplitude modulation. The amplitude of the carrier waveform varies with the amplitude of the modulating waveform. / FM: frequency modulation. The frequency of the carrier waveform varies with the amplitude of the modulating waveform. / Sine, Square, Ramp, Built-in waveforms or Arb waveform (except DC) can be used as the carrier waveform. / You can use the [:SOURce[<n>]]:MOD:AM:INTernal:FUNCtion or [:SOURce[<n>]]:MOD:FM:INTernal:FUNCtion command to selelct Sine, Square, Triangle or Noise as the modulating waveform.
Return format	The query returns AM or FM.
Syntax	:MOD:TYPe AM /*Set the modulation type of source 1 to AM*/ / :MOD:TYPe? /*The query returns AM*/

## [:SOURce[<n>]]:MOD:AM[:DEPTh]
Syntax	[:SOURce[<n>]]:MOD:AM[:DEPTh] <depth> / [:SOURce[<n>]]:MOD:AM[:DEPTh]?
Description	Set or query the AM modulation depth (indicates the amplitude variation degree and is expressed as a percentage) of the specified source channel.
Parameter	Name	Type	Range	Default
	[<n>]	Discrete	{1|2}	If omitted, the operation is performed on source 1 by default
	<depth>	Real	0 to 120	100
Explanation	In 0% modulation, the output amplitude is half of the carrier waveform amplitude. / In 100% modulation, the output amplitude is equal to the carrier waveform amplitude. In >100% modulation, envelop distortion which should be avoided in the real circuit will occur and the output amplitude of the instrument would not exceed 5Vpp (50Ω load).
Return format	The query returns an integer.
Syntax	:MOD:AM 80 /*Set the AM modulation depth of source 1 to 80%*/ / :MOD:AM? /*The query returns 80*/

## [:SOURce[<n>]]:MOD:AM:INTernal:FREQuency
## [:SOURce[<n>]]:MOD:FM:INTernal:FREQuency
Syntax	[:SOURce[<n>]]:MOD:AM:INTernal:FREQuency <frequency> / [:SOURce[<n>]]:MOD:AM:INTernal:FREQuency? / [:SOURce[<n>]]:MOD:FM:INTernal:FREQuency <frequency> / [:SOURce[<n>]]:MOD:FM:INTernal:FREQuency?
Description	Set or query the modulating waveform frequency of AM or FM of the specified source channel. The default unit is Hz.
Parameter	Name	Type	Range	Default
	[<n>]	Discrete	{1|2}	If omitted, the operation is performed on source 1 by default
	<frequency>	Real	1Hz to 50kHz	1kHz
Explanation	Sending the [:SOURce[<n>]]:MOD:TYPe command can set the modulation type. / AM: amplitude modulation. The amplitude of the carrier waveform varies with the amplitude of the modulating waveform. / FM: frequency modulation. The frequency of the carrier waveform varies with the amplitude of the modulating waveform. / Sending [:SOURce[<n>]]:MOD:AM:INTernal:FUNCtion or [:SOURce[<n>]]:MOD:FM:INTernal:FUNCtion can selelct Sine, Square, Triangle or Noise as the modulating waveform.
Return format	The query returns an integer.
Syntax	:MOD:AM:INTernal:FREQuency 100 /*Set the modulating waveform frequency of AM of source 1 to 100Hz*/ / :MOD:AM:INTernal:FREQuency? /*The query returns 100*/

## [:SOURce[<n>]]:MOD:AM:INTernal:FUNCtion
## [:SOURce[<n>]]:MOD:FM:INTernal:FUNCtion
Syntax	[:SOURce[<n>]]:MOD:AM:INTernal:FUNCtion <wave> / [:SOURce[<n>]]:MOD:AM:INTernal:FUNCtion? [:SOURce[<n>]]:MOD:FM:INTernal:FUNCtion <wave> / [:SOURce[<n>]]:MOD:FM:INTernal:FUNCtion?
Description	Set or query the modulating waveform of AM or FM of the specified source channel.
Parameter	Name	Type	Range	Default
	[<n>]	Discrete	{1|2}	If omitted, the operation is / performed on source 1 by default
	<wave>	Discrete	{SINusoid|SQUare|TRIangle|NOISe}	SINusoid
Explanation	Sine (SINusoid), Square (SQUare), Triangle (TRIangle) or Noise (NOISe) can be selected as the modulating waveform. You can set the frequency of the modulating waveform by sending [:SOURce[<n>]]:MOD:AM:INTernal:FREQuency or [:SOURce[<n>]]:MOD:FM:INTernal:FREQuency. / Sending the [:SOURce[<n>]]:MOD:TYPe command can set the modulation type. / AM: amplitude modulation. The amplitude of the carrier waveform varies with the amplitude of the modulating waveform. / FM: frequency modulation. The frequency of the carrier waveform varies with the amplitude of the modulating waveform.
Return format	The query returns SIN, SQU, TRI or NOIS.
Syntax	:MOD:AM:INTernal:FUNCtion SQUare /*Set the modulating waveform of AM of source 1 to square*/ / :MOD:AM:INTernal:FUNCtion? /*The query returns SQU*/

## [:SOURce[<n>]]:MOD:FM[:DEVIation]
Syntax	[:SOURce[<n>]]:MOD:FM[:DEVIation] <dev> / [:SOURce[<n>]]:MOD:FM[:DEVIation]?
Description	Set or query the FM frequency deviation of the specified source channel. The default unit is Hz.
Parameter	Name	Type	Range	Default
	[<n>]	Discrete	{1|2}	If omitted, the operation is performed on source 1 by default
	<dev>	Real	0Hz to the carrier waveform frequency	1kHz
Explanation	Sending [:SOURce[<n>]]:FREQuency[:FIXed] can set the carrier waveform frequency and sending [:SOURce[<n>]]:MOD:FM:INTernal:FREQuency can set the FM modulation frequency. / When the modulating waveform amplitude reaches its maximum, the carrier waveform frequency increases by the “frequency deviation”. When the modulating waveform amplitude reaches its minimum, the carrier waveform frequency decreases by the “frequency deviation”. / You can only set the FM frequency deviation when the modulation type of the specified signal source channel is set to FM.
Return format	The query returns an integer.
Syntax	:MOD:FM 100 /*Set the FM frequency deviation of source 1 to 100Hz*/ / :MOD:FM? /*The query returns 100*/

## [:SOURce[<n>]]:APPLy?
Syntax	[:SOURce[<n>]]:APPLy?
Description	Query the output configurations of the specified source channel.
Parameter	Name	Type	Range	Default
	[<n>]	Discrete	{1|2}	If omitted, the operation is performed on source 1 by default
Return Format	The query returns the output configurations in “<waveform / name>,<frequency>,<amplitude>,<offset>,<start phase>” format. If the corresponding parameter does not exist, it will be replaced by "DEF".
Example	:APPLy? /*The query returns SIN,1000.000000,1.000000,0.000000,0.000000*/

## [:SOURce[<n>]]:APPLy:NOISe
## [:SOURce[<n>]]:APPLy:PULSe
## [:SOURce[<n>]]:APPLy:RAMP
## [:SOURce[<n>]]:APPLy:SINusoid
## [:SOURce[<n>]]:APPLy:SQUare
## [:SOURce[<n>]]:APPLy:USER
Syntax	[:SOURce[<n>]]:APPLy:NOISe [<amp>[,<offset>]] / [:SOURce[<n>]]:APPLy:PULSe [<freq>[,<amp>[,<offset>[,<phase>]]]] / [:SOURce[<n>]]:APPLy:RAMP [<freq>[,<amp>[,<offset>[,<phase>]]]] / [:SOURce[<n>]]:APPLy:SINusoid [<freq>[,<amp>[,<offset>[,<phase>]]]] / [:SOURce[<n>]]:APPLy:SQUare [<freq>[,<amp>[,<offset>[,<phase>]]]] / [:SOURce[<n>]]:APPLy:USER [<freq>[,<amp>[,<offset>[,<phase>]]]]
Description	Configure the specified source channel to output a signal with the specified waveform and parameters.
Parameter	Name	Type	Range	Default
	[<n>]	Discrete	{1|2}	If omitted, the operation is performed on source 1 by default
	<freq>	Real	Sine: 0.1Hz to 25MHz / Square: 0.1Hz to 15MHz / Pulse: 0.1Hz to 1MHz / Ramp: 0.1Hz to 100kHz / Arbitrary waveform: 0.1Hz to 10MHz	1kHz
	<amp>	Real	Related to the output impedance: / HighZ: 20mVpp to 5Vpp / 50Ω: 10mVpp to 2.5Vpp	5Vpp
	<offset>	Real	Related to the output impedance and amplitude: / HighZ: ±(2.5V-current amplitude/2) / 50Ω: ±(1.25V-current amplitude/2)	0μVdc
	<phase>	Real	0° to 360°	0°
Explanation	These commands are used to select the waveform shape. / NOISe: select Noise PULSe: select Pulse / RAMP: select Ramp / SINusoid: select Sine / SQUare: select Square / USER: select Arbitrary waveform / <freq>: set the frequency of the specified waveform (Noise does not have this parameter). The default unit is Hz; / <amp>: set the amplitude of the specified waveform. The default unit is Vpp; <offset>: set the DC offset of the specified waveform. The default unit is VDC; <phase>: set the start phase of the specified waveform (Noise does not have this parameter). The default unit is degree (°). / Users can omit one or multiple parameters. When all of the parameters are omitted, the commands only select the waveform shape but do not modify the parameters. / The four parameters (<freq>, <amp>, <offset> and <phase>) are in order. You can not omit one parameter and set the one/ones behind it. For example, you can not omit <freq> and set <amp> directly.